## Slide 1: Sequential Building Blocks

## Slide 2: Index
Building Blocks
Counters
Digitally Controlled Oscillator (DCO)
Shift Registers
Scan Chains
Memory Arrays
Bit Cell
Dynamic Random Access Memory (DRAM)
Static Random Access Memory (SRAM)
Register Files
Read Only Memory (ROM)
Programmable ROM (PROM)
Lookup tables (LUT)
Programmable Logic Array (PLA)
Field Programmable Gate Array (FPGA)

## Slide 3: Building Blocks
Like Combinational logic, also Sequential logic is often grouped into larger building blocks to build more complex systems
  principles of abstraction, hierarchy, modularity, and regularity
  hiding the unnecessary gate-level details to emphasize the function of the building block
  hierarchically assembled from simpler components
  a well-defined interface and can be treated as a black box
Examples:
  Counters
  Registers
  Memory
  PLA
  FPGA
We will use many of these building blocks to build a microprocessor

## Slide 4: Counters
A device that advances through all 2N possible outputs in binary order
  incrementing on the rising edge of the clock
  Reset initializes the output to 0
A possible implementation composed of an adder and a resettable register
  on each cycle, the counter adds 1 to the value stored in the register
The most significant bit toggles every 2N cycles
  it can reduces the frequency of the clock by a factor of 2N
  useful for slowing down fast signals
  a digital system with a 50MHz clock, can be slowed with a 24-bit counter to produce a 2.98Hz signal that blinks a LED at a rate the human eye can observe

## Slide 5: Digitally Controlled Oscillator (DCO)
A counter generalization to produce arbitrary frequencies
A N-bit counter that adds p on each cycle, rather than 1
  if the clock has frequency fclk, the most significant bit now toggles at fout = fclk * p/2N
Selecting p and N, we can produce an output of any frequency
  larger N gives more precise control at the expense of more hardware
Suppose we have a 50 MHz clock and want to produce a 500 Hz output
  consider using an N=24 or 32 bit counter
  we want p/2N = 500Hz/50MHz = 0.00001
  if N=24, choose p=168 to get fout=500.68Hz
  if N=32, choose p=42950 to get fout=500.038 Hz

## Slide 6: Shift Registers (1)
A device that shift in a new bit on each clock edge
  on each rising edge of the clock, a new bit is shifted in from Sin and all the subsequent contents are shifted forward
  the last bit in the shift register is available at Sout
It can be constructed from N flip-flops connected in series
Don’t confuse shift registers with shifters
  shifters are un-clocked combinational blocks that shift an input by a specified amount
Can be viewed as serial-to-parallel converter
  the input is provided serially (one bit at a time) at Sin
  after N cycles, the past N inputs are available in parallel at Q

## Slide 7: Shift Registers (2)
A related circuit is a parallel-to-serial converter
  it loads N bits in parallel
  then shifts them out one at a time
A shift register can be modified to perform both serial-to-parallel and parallel-to-serial operations by adding a parallel input DN−1:0 and a control signal
  when Load is asserted, the flip-flops are loaded in parallel from the D inputs
  otherwise, the shift register shifts normally

## Slide 8: Scan Chains
Testing combinational circuits is relatively straightforward
  known inputs (test vectors) are applied and outputs are checked
Testing sequential circuits is more difficult because the circuits have state
  a large number of cycles of test vectors may be needed to put the circuit into a state
    testing that the msb of a 32-bit counter requires 231 clock pulses!
A solutions: directly control the state
  all flip-flops are connected together into a shift register called a scan chain
    in normal operation, flip-flops load data from their input D
    in test mode, flip-flops serially shift contents using Sin and Sout
The example:
  32-bit counter can be tested by shifting in the pattern 011111…111 in test mode, counting for one cycle, then shifting out the result, which should be 100000…000
  this requires 32 + 1 + 32 = 65 cycles

## Slide 9: Memory (1)
Digital systems require memories to store data used and generated by circuits
  registers are a kind of memory that stores small amounts of data
Memory arrays can efficiently store large amounts of data
Memories are classified based on how they store bits
  Random Access Memory (RAM)
    volatile: loses data when the power is turned off
  Read Only Memory (ROM)
    non-volatile: retains its data indefinitely, even without a power source
Names for historical reasons: no longer very meaningful
  RAM accesses data with the same delay, in contrast with sequential access memory (e.g. tape recorder accesses nearby data more quickly than faraway data)
  ROM historically could only be read, but not written
These names are confusing
  ROMs are also randomly accessed…
  worse yet, modern ROMs can be written as well as read…
Just one important distinction: volatile and non-volatile
Three types of memory arrays:
  Dynamic Random Access Memory (DRAM)
  Static Random Access Memory (SRAM)
  Read Only Memory (ROM)
  each type differs in the way it stores data

## Slide 10: Memory (2)
1956, IBM 305 RAMAC
5MB Hard Drive
$3,200 (equivalent to $30,874 today)… …per month

## Slide 11: Memory Arrays
Memory is organized as a two-dimensional array of memory cells
  the memory reads or writes the contents of one of the rows of the array
The row is specified by an address
The value read or written is called data
An array with N-bit addresses and M-bit data has 2N rows and M columns
Each row of data is called a word
  the array contains 2N M-bit words
The depth of an array is the number of rows
the width is the number of columns, also called the word size
The size of an array is given as depth * width
Example:
  a memory array with two address bits and three data bits
  the two address bits specify one of the four rows (data words)
  each data word is three bits wide
  it is a 4-word * 3-bit array, or simply 4 × 3 array

## Slide 12: Bit Cell (1)
Memory arrays are built as an array of bit cells
  each of which stores 1 bit of data
Each bit cell is connected to a wordline and a bitline
  for each combination of address bits, the memory asserts a single wordline that activates the bit cells in that row
  when the wordline is HIGH, the stored bit transfers to or from the bitline
  otherwise, the bitline is disconnected from the bit cell
The circuitry to store the bit varies with memory type
To read a bit cell
  the bitline is left floating (Z)
  then the wordline is turned ON, allowing the stored value to drive the bitline
To write a bit cell
  the bitline is strongly driven to the desired value
  then, the wordline is turned ON, connecting the bitline to the stored bit
  the strongly driven bitline overpowers the contents of the bit cell, writing the desired value into the stored bit

## Slide 13: Bit Cell (2)
The figure shows the internal organization of a 4 * 3 memory array

## Slide 14: Dynamic Random Access Memory (DRAM)
DRAM stores data as a charge on a capacitor
  transistor behaves as a switch
  connects or disconnects the capacitor from the bitline
when the capacitor is charged to VDD, the stored bit is 1
when it is discharged to GND, the stored bit is 0
Upon a read, data are transferred from the capacitor to the bitline
Upon a write, data values are transferred from the bitline to the capacitor
Reading destroys the bit stored on the capacitor
  data must be restored (rewritten) after each read
  even when it is not read, the contents must be refreshed (read and rewritten)
    every few milliseconds
    the charge on the capacitor gradually leaks away

## Slide 15: Static Random Access Memory (SRAM)
The data bit is stored on cross-coupled inverters
Each cell has two outputs, bitline and bitline
  when the wordline is asserted, both transistors turn on
  data values are transferred to or from the bitlines
Do not need to be refreshed

## Slide 16: Memory comparison
Flip-flops, SRAM, and DRAM are all volatile memories, but each has different area and delay characteristics
Flip-flop data is available immediately in output, but it takes at least 20 transistors
DRAM is slower
  must wait for charge to move (relatively) slowly from the capacitor
  must refresh data periodically and after a read
Today, modern DRAM technologies (synchronous and double data rate, DDR)
  uses both rising and falling edges of the clock to access data
  first standardized in 2000 (100 MHz), today (2021) speeds over 3 GHz
The best memory type for a particular design depends on the speed, cost, and power constraints

## Slide 17: Register Files
A set of registers used to store temporary variables
Usually built as a small, multi-ported SRAM array
  more compact than an array of flip-flops
  multi-ported means that can access several addresses simultaneously
For example, a 32-register with 32-bit three-ported register file
  two read ports (A1/RD1 and A2/RD2)
  one write port (A3/WD3)
  the 5-bit addresses (A1, A2, A3) can access all 25 = 32 registers
  two registers can be read and one register written simultaneously
Sometimes, a particular register is hardwired to always read the value 0
  because 0 is a commonly used constant

## Slide 18: Read Only Memory (ROM) (1)
ROM stores a bit as the presence or absence of a transistor
To read the cell:
  the bitline is weakly pulled HIGH
  then, the wordline is turned ON
    if the transistor is present, it pulls the bitline LOW
    if it is absent, the bitline remains HIGH
The contents of a ROM can be indicated using dot notation

## Slide 19: Programmable ROM
Places a transistor in every bit cell, but provides a way to connect or disconnect the transistor to ground
User programs the ROM by applying a high voltage to selectively blow fuses
  if the fuse is present, transistor is connected to GND and the cell holds 0
  if the fuse is destroyed, transistor is disconnected from ground and the cell holds 1
One-time programmable ROM
  because the fuse cannot be repaired once it is blown
Exist also reversible mechanism for connecting or disconnecting the transistor

## Slide 20: Re-programmable ROM
Erasable PROMs (EPROM)
  replace the transistor and fuse with a floating-gate transistor
    not physically attached to any other wires
    when high voltages are applied, electrons tunnel through an insulator onto the floating gate, turning on the transistor and connecting the bitline to the wordline
    when exposed to ultraviolet light (half an hour), the electrons are knocked off the floating gate, turning the transistor off
    these actions are called programming and erasing
Electrically erasable PROMs (EEPROM) and Flash memory
  use similar principles but include circuitry for erasing and programming
  in 2021, Flash cost about $0.1 per GB, and price is dropping
    a way to store large amounts of data in portable battery-powered systems
ROMs are not really read only: they can be programmed
  difference between RAM and ROM: ROMs take a longer time to write but are non-volatile

## Slide 21: Lookup tables (LUT)
Memory arrays can also perform combinational logic functions
  each address corresponds to a row in the truth table
  each data bit corresponds to an output value
    Data2 is the XOR of the two address inputs
    Data0 is the NOR of the two inputs
A 2N-word × M-bit memory can perform any combinational function of N inputs and M outputs
The following figure shows a LUT (4-word × -bit) to perform the function Y = AB

## Slide 22: Programmable Logic Array (PLA)
Like memory, gates can be organized into regular arrays
  if connections are made programmable, they can be configured to perform any function
PLA implement two-level combinational logic in sum-of-products form
  the inputs (in true and complementary form) drive an AND array
    which produces implicants
  the implicants, in turn, are ORed together to form the outputs
An M×N×P-bit PLA has M inputs, N implicants, and P outputs

## Slide 23: Programmable Logic Array (PLA)
The following figure shows the a 3×3×2-bit PLA performing functions X = A B C + A B C and Y = A B
ROMs can be viewed as a special case of PLAs
  A 2M-word×N-bit ROM is simply an M×2M×N-bit PLA
  the decoder behaves as an AND plane that produces all 2M minterms
  the ROM array behaves as the OR plane that produces the outputs
If function does not depend on all minterms, PLA is smaller than a ROM
PLAs have largely been displaced by FPGAs, which are more flexible and efficient

## Slide 24: Field Programmable Gate Array (FPGA) (1)
An array of reconfigurable logic elements (LE)
  user can implement designs on the FPGA employing either Hardware Description Language (HDL) or a schematic
  each LE can be configured to perform combinational or sequential functions
  LEs are surrounded by input/output elements (IOE) for interfacing with the outside world
    IOEs inputs and outputs to pins on the chip package
  LEs can connect to other LEs and IOEs through programmable routing channels.
FPGAs are more powerful and more flexible than PLAs
  can implement both combinational and sequential logic
  can implement multilevel logic functions (not just two-level logic)
  can integrate other useful features
    built-in multipliers, high-speed I/Os, data converters, large RAM arrays, and processors

## Slide 25: Field Programmable Gate Array (FPGA) (2)
The following figure shows a single LE from Intel’s Cyclone IV FPGA
  a 4-input lookup table (LUT)
  a 1-bit register
  configurable multiplexers to route signals
The FPGA is configured by
  loading values into the LUT, it perform any function of up to four variables
  determining how the multiplexers route data through the LE and to neighbouring LEs and IOEs
For example
  LUT may receive one input from either data 3 or the output of the LE register
  other three inputs always come from data1, data2, and data4
  inputs come from IOEs or from the outputs of other LEs
  LUT output either goes directly to the LE output or it can be fed through the flip-flop
  flip-flop input comes from LUT output or the data 3 input or the register output of the previous LE

## Slide 26: Field Programmable Gate Array (FPGA) (3)
Other brands of FPGA are organized somewhat differently, but the same general principles apply.
  for example, Xilinx’s 7-series FPGAs use 6-input LUTs instead of 4-input LUTs
The designer configures an FPGA by first creating a schematic or HDL description of the design
  the design is then synthesized onto the FPGA
  synthesis tool determines how the LUTs, multiplexers, and routing channels should be configured to perform the specified functions
This configuration information is then downloaded to the FPGA
  Cyclone IV FPGAs store their configuration information in SRAM and then are easily reprogrammed
  FPGA may download its SRAM contents from a computer or from an EEPROM chip when the system is turned on
    some manufacturers include an EEPROM directly on the FPGA or use one-time programmable fuses to configure the FPGA
DEEDS is capable of creating an HDL description of your schematic that can be deployed on a real FPGA, as we will see in the next semester!

## Slide 27: Exercises
Ex1: Configure one or more Cyclone IV LE to perform the following functions X = A B C + A B C and Y = A B
Solution
  Two LEs (one computes X and the other computes Y
    First LE
      inputs data1, data2, and data3 are A, B, and C
      data4 is a don’t care but must be tied to something, so it is tied to 0.
    second LE
      inputs data1 and data2 are A and B
      other inputs are don’t cares and are tied to 0
  The final multiplexers select the combinational outputs from the LUTs to produce X and Y