## Slide 1: Combinational Building Blocks

## Slide 2: Index
Building Block definition
Multiplexer
Decoders
Adders
Subtractor
Comparators
Arithmetic/Logical Unit (ALU)
Shifters and Rotators
Multiplier and divider
Floating-Point Addition

## Slide 3: Building Block Definition
Combinational logic can be grouped in larger building blocks to build more complex systems
Abstraction, hierarchy, modularity, and regularity
  abstract (hide) gate-level details to emphasize the function of the module (block)
  hierarchically assembled from simpler components
  well-defined interfaces in order to use them as a black boxes
Examples:
  seven-segment display decoders (already considered)
  multiplexers
  decoders
  arithmetic circuits
We will use many of these building blocks to build a microprocessor

## Slide 4: Multiplexer (mux)
A device that choose an output among several possible inputs, based on the value of a select signal
A 2:1 multiplexer has two data inputs D and one output Y and a select signals S:
  if S=0, Y=D0
  if S=1, Y=D1

## Slide 5: Wider multiplexer
A 4:1 multiplexer has four data inputs and one output and two select signals are needed to choose among the four data inputs
  it can be built using sum-of-product logic, or multiple 2:1 multiplexers
Wider multiplexers (8:1 and 16:1) can be built by expanding the method
  in general, a N:1 multiplexer needs log2N select lines

## Slide 6: Multiplexer example
A multiplexer is like a data router: connects only one input at a time, allowing different data sources to share the same output line efficiently
This makes it possible to handle many inputs in a controlled, sequential way without needing separate circuits for each one

## Slide 7: Multiplexer Logic (1)
Multiplexers can be used as lookup tables to perform logic functions
For example, we can implement a two-input AND gate:
  A and B serve as select lines
  inputs are connected to 0 or 1, according to the truth table
  changing the data inputs, the multiplexer can be reprogrammed to perform a different function
In general, a 2N-input multiplexer can be programmed to perform any N-input logic function by applying 0 and 1 to the appropriate data inputs

## Slide 8: Multiplexer Logic (2)
We can cut the multiplexer size in half, using only a 2N–1 input multiplexer to perform any N-input logic function
Provide one of the literals to the multiplexer inputs:

## Slide 9: Multiplexer Logic (3)
As an example, implement the following function
  using a 8:1 multiplexer:
  and a 4:1 multiplexer:

## Slide 10: Multiplexer VHDL

## Slide 11: Decoder
A device with N inputs and 2N outputs that asserts exactly one of its outputs depending on the input combination
For example, consider a 2:4 decoder
  when A1:0 = 00, Y0 is 1
  when A1:0 = 01, Y1 is 1
  and so forth
The outputs are called one-hot, because just one is “hot” (HIGH) at a given time
In the implementation, each gate depends on either the true or the complementary form of each input
  an N:2N decoder can be constructed from 2N N-input AND gates that accept the various combinations of true or complementary inputs
  each output in a decoder represents a single minterm
    for example, Y3 represents the minterm A1 A0.

## Slide 12: Decoder VHDL

## Slide 13: Decoder example
A decoder can be used to control which of several lines is “on” based on the binary value of the input. It can be used in memory address selection:

## Slide 14: Decoder Logic
Decoders can be combined with OR gates to build logic functions
  because each output of a decoder represents a single minterm, the function is built as the OR of all of the minterms in the function
  example: a two-input XNOR function using a 2:4 decoder and a single OR gate
An N-input function with M 1s in the truth table can be built with an N:2N decoder and an M-input OR.

## Slide 15: Half and Full Adders
Addition is one of the most common operations in digital systems
Half adder
  two inputs, A and B, and two outputs, S and Cout
  S is the sum of A and B
  Cout is the eventual carry out
In a multi-bit adder, Cout is added (carried) in to the next most significant bit
  half adder lacks a Cin input to accept the Cout of the previous column
Full Adder
  accepts also the carry in Cin

## Slide 16: Carry Propagate Adder
A N-bit adder that sums two N-bit inputs and a carry-in to produce an N-bit result and a carry-out
  the carry bit propagates into the adder
  drawn like a full adder except that input/output are busses rather than single bits
Simplest way to build: chain together N full adders (Ripple-Carry Adder RCA)
  Couy of one stage acts as the Cin of the next stage
A good application of modularity and regularity
  full adder module is reused many times to form a larger system
It is slow when N is large.
  S3 depends on C2, which depends on C1, and so forth
  the delay of the adder triple = N * tFA grows directly with the number of bits

## Slide 17: Carry-Lookahead Adder (1)
RCA are slow because the carry must propagate:
The idea is to divide the adder into blocks and determine the carry out of a block as soon as the carry in is known
  it looks ahead across the blocks rather than wait to ripple through all the full adders

## Slide 18: Carry-Lookahead Adder (2)
Carry-Lookahead Adder CLA use generate (G) and propagate (P) signals
A column “generates” a carry if it produces a carry independent of its carry-in
  both input are 1 -> Gi = Ai AND Bi
A column “propagates” a carry if it produces a carry whenever there is a carry-in
  either one of the input is 1 -> Pi = Ai OR Bi

## Slide 19: Carry-Lookahead Adder (2)
We can extend to multiple-bit blocks
  a block “generates” a carry if it produces a carry out independent of the carry-in
  a block “propagate” a carry if it produces a carry out whenever there is a carry-in
A block j:i (spanning columns i through j) generates a carry
  if the most significant column generates a carry
  if the previous column generated a carry and the most significant column propagates it
  and so forth
  Gj:i = Gj + Pj(Gj-1 + Pj-1 (Gj-2 + Pj-2 ( …. (Gi+2 + Pi+2(Gi+1 + Pi+1Gi))
    e.g. G7:4 = G7 + P7(G6 + P6(G5 + P5G4)
A block i:j propagates a carry
  if all the columns in the block propagate the carry
  Pj:i = PjPj-1Pj-2…Pi+2 Pi+1 Pi
    e.g. P3:0 = P3P2P1P0
So, we can quickly compute the carry out of the block
  Cj = Gj:i + Pj:iCi-1

## Slide 20: Carry-Lookahead Adder (3)

## Slide 21: Carry-Lookahead Adder (4)
A 32-bit carry-lookahead adder composed of eight 4-bit blocks:
Each block contains a 4-bit ripple-carry adder and the lookahead circuit to compute the carry out of the block given the carry-in
All blocks compute column generate and propagate signals simultaneously
Then Cin advances to Cout through each block until the last
  Cin proceeds through the lookahead gates to produce C3
  C3 proceeds through its lookahead block to produce C7
  C7 proceeds through its lookahead block to produce C11
  and so on until C27, the carry-in to the last block
The last block contains a short ripple-carry adder (no more the lookahead logic)

## Slide 22: Carry-Lookahead Adder delay
An N-bit adder divided into k-bit blocks has a delay
  tpg is the delay to generate signals Pi and Gi
  tpg_block is the delay to to generate signals Pj:i and Gj:i for a k-bit block
  tlookahead is the delay from Cin to Cout through the logic of the k-bit CLA block
tCLA = tpg + tpg_block + (N/k -1) tlookahead + k tFA
For N > 16, the carry-lookahead adder is much faster than the ripple-carry adder
  however, the adder delay still increases linearly with N
Faster adders require more hardware and therefore are more expensive and power-hungry
  these trade-offs must be considered when choosing an appropriate adder for a design

## Slide 23: Ripple-Carry Adder vs Carry-Lookahead Adder
Compare the delays of a 32-bit ripple-carry adder and a 32-bit carry-lookahead adder with 4-bit blocks
Assume that each gate delay is 100ps and that a full adder delay is 300ps
The propagation delay of the 32-bit ripple-carry adder is
  triple = N * TFA = 32 * 300ps = 9.6 ns
The carry-lookahead adder has
  tpg = 100ps (one AND or one OR)
  tpg_block = 6 * 100 ps = 600ps (six AND/OR gates)
  tlookahead = 2 * 100 ps = 200ps (one OR and one AND)
  tCLA=tpg+tpg_block+(N/k-1)tlookahead+ktFA = 100 + 600 + (32/4 - 1)*200 + 4*300 = 3.3ns
The carry-lookahead adder is almost 3 times faster than the ripple-carry adder

## Slide 24: Subtractor
Performed by taking the two’s complement of the second number, then adding
To compute Y = A − B
  first create the two’s complement of B
    invert the bits of B to obtain B
    add 1 to get −B = B + 1
  add this quantity to A
    Y = A + B + 1 = A − B
We can use a single carry-lookahead adder by adding A + B with Cin = 1

## Slide 25: Comparators (1)
Determines whether two binary numbers are equal or if one is greater or less than the other
  receives two N-bit binary numbers A and B
  an equality comparator produces a single output, indicating A is equal to B
  a magnitude comparator produces one or more outputs, indicating the relative values of A and B
The equality comparator is the simpler piece of hardware
  it checks whether the corresponding bits in each column of A and B are equal
    using XNOR gates
  the numbers are equal if all the columns are equal

## Slide 26: Comparators (2)
Magnitude comparison of signed numbers is usually done by computing A − B and looking at the sign (most significant bit) of the result
  if the result is negative (i.e., the sign bit is 1), then A is less than B
  otherwise, A is greater than or equal to B
This comparator functions incorrectly upon overflow
  overflow occurs when
    the two inputs have different signs
    and the sign of the subtraction result has a different sign than the A input

## Slide 27: Arithmetic/Logical Unit (1)
ALU combines a variety of mathematical and logical operations into a single unit
  addition, subtraction, AND, and OR operations
  control signal to specifies the function to perform
  the heart of most computer systems
The following implementation contains
  an N-bit adder, N 2-input AND and OR gates

## Slide 28: Arithmetic/Logical Unit (2)
ALU can produce flags to provide information about the result
Z (zero)
  all the bits of the output are 0
N (negative)
  the most significant bit of the output
C (carry)
  adder produces a carry out and the ALU is performing addition or subtraction
V (overflow)
  overflow occurs when the addition of two same signed numbers produces a result with the opposite sign
    ALU is performing addition or subtraction (C1=0)
    A and Sum have opposite signs
    A and B have the same sign, and the adder is performing addition (C0=0)
    or A and B have opposite sign, and the adder is performing subtraction (C0=1)

## Slide 29: Arithmetic/Logical Unit (3)

## Slide 30: Arithmetic/Logical Unit (4)
The ALU flags can also be used for comparisons
  ALU computes A-B and look at the flags:
    (1) if Z is asserted, the result is 0, so A==B
    (2) otherwise, A is not equal to B
    (3) magnitude comparison is messier, we see whether the answer is negative (N). However, if overflow occurs, the N flag will be incorrect. Hence, A is less than B if the answer is negative and there is no overflow or if the answer is positive but overflow occurred
    (4) A is less then or equal to B if occur the OR of condition (1) and (3)
    (5) A is greater then B, if it is not less then or equal to B, the negation of condition (4)
    (6) A is greater then or equal to B, if it is not less then B, the negation of condition (3)
Processors can use combinations of status bits for conditional branching (e.g., checking if a value is less than zero or within bounds)
Many variations on this basic ALU exist that support other functions

## Slide 31: Shifters (1)
Shifters moves binary data, crucial in arithmetic operations, logical operations, and data manipulation. The main types are:
  logical shifter: shifts all bits to the left (or right), inserting a 0 into lsb (or msb) and discarding msb (or lsb)
  arithmetic shifter: like a logical shift with sign bit preserved if possible
A left shift by N bits multiplies the number by 2N
  0000112 << 4 = 1100002 is equivalent to 310 × 24 = 4810
A right shift by N bits multiplies the number by 2N
  111002 >>> 2 = 111112 is equivalent to −410/22 = −110

## Slide 32: Shifters (2)
An N-bit shifter can be built from N N:1 multiplexers
Depending on the value of a log2(N)-bit shift amount control signal, the output receives the input shifted by 0 to N-1 bits

## Slide 33: Rotators
Rotator rotates (left or right) a number in a circle such that empty spots are filled with bits shifted off the other end

## Slide 34: Multiplier (1)
Multiplication of 1-bit numbers is equivalent to the AND operation
A N×N multiplier produces a 2N-bit result
  partial product is the AND of a single multiplier bit (B3, B2,…) with the multiplicand bits (A3, A2,…)
  each partial products is added to the shifted next partial product
    B0 AND (A3, A2, A1, A0) is added to B1 AND (A3, A2, A1, A0)
Considering an unsigned 4 × 4 multiplier

## Slide 35: Multiplier (2)
Considering an unsigned 4 × 4 multiplier

## Slide 36: Division (1)
The most complex operation to perform among all the arithmetic operations
  the basic idea is the same as long division in decimal
    how many times the divisor can fit into sections of the dividend without exceeding it?
    each time it fits, we add a 1 to the quotient
    if it doesn’t fit, we add a 0
This is the restoring division algorithm

## Slide 37: Division (2)

## Slide 38: Floating-Point Addition (1)

## Slide 39: Floating-Point Addition (2)
Floating-point arithmetic is usually done in hardware to make it fast
  floating-point unit (FPU)
  typically, distinct from the central processing unit (CPU)
The infamous floating-point division bug (1994)
  the processor returns incorrect binary floating point results when dividing certain pairs of high-precision numbers…
  missing values in a lookup table used by the FPU's division algorithm led to calculations acquiring small errors
  these errors only occur rarely producing small deviations from the correct output
  in certain circumstances the errors can occur frequently and lead to more significant deviations
  Byte magazine estimated that 1 in 9 billion floating point divides with random parameters would produce inaccurate results
  December 1994, Intel recalled the defective processors in what was the first full recall of a computer chip: it cost $475 million