## Slide 1: The Digital Abstraction

## Slide 2: Index
Managing Complexity
  Abstraction
  Discipline
  The Three -Y’s
Digitalization
  Sampling
  Quantization
Sensors
Amount of information
Boole Algebra

## Slide 3: Complexity
Microprocessors revolutionized our world during the past three decades
  laptop computers today have far more capability than a room-sized mainframe of yesteryear
  automobiles contain about 100 microprocessors
  worldwide semiconductor industry sales have grown from US $21 billion in 1985 to $400 billion in 2020
Digital systems are built from millions or billions of transistors
  no human being could understand these systems by writing equations describing the movement of electrons in each transistor and solving all of the equations simultaneously
  we need to learn to manage complexity to understand how to build a digital system (like a microprocessor) without getting lost in a morass of detail

## Slide 4: Abstraction
Hiding details when they are not important!
  lowest level is physics: motion of electrons (quantum mechanics and Maxwell’s equations)
  electron devices (transistors) have well-defined connection points (terminals), we can ignore the individual electrons
  devices are assembled to create analog circuits (amplifiers) that input and output continuous voltages
  digital circuits (logic gates) restrict the voltages to discrete ranges (indicate 0 and 1)
  from digital circuits we build more complex components (adders or memories)
  the micro-architecture level describes the system from data and operations perspective
  the architecture level describes the system from the programmer’s perspective
  …ad so on: operating system (handles hard drive or managing memory) and finally, application software…

## Slide 5: Discipline
Intentionally restricting the design choices so that one can work more productively at a higher level of abstraction
Famous example (1908): Ford Model T
  previous cars were hand-crafted by skilled men
    time-consuming and expensive process
  Henry Ford focused on mass production with interchangeable parts and moving assembly lines
    by limiting components to a standardized set with well-defined tolerances, cars could be assembled much faster and with less skill
    car builders no longer concerned with lower levels of abstraction (such as, fitting a door to a non-standardized opening)
  Ford’s famous saying: “Any customer can have a car painted any color that he wants so long as it is black”

## Slide 6: The three «-y»
Hierarchy: dividing a system into modules, then further subdividing each of these modules until the pieces are easy to understand
Modularity : modules should have well-defined functions and interfaces, so that they connect easily without unanticipated side effects
Regularity: seek uniformity among modules, common modules are reused many times, reducing the number of distinct modules that must be designed
Ford Model T example:
  we can break the car into components: chassis, engine, and seats; the engine contains cylinders, carburetor, and cooling system; the carburetor contains fuel and air intakes, a throttle and so forth…the complex system is recursively broken down into simple interchangeable components (hierarchy)
  the coupling nut has a function of holding the fuel feed line to the intake elbow and it is of a standardized diameter and thread pitch, tightened to a standardized torque by a standardized wrench (modularity)
  a car maker can buy the nut from many different suppliers, as long as the correct size is specified (regularity)

## Slide 7: The Digital Abstraction
Digital circuits use discrete voltages, analog circuits use continuous voltages
  a subset of analog circuits
  much simpler to design
By limiting ourselves to digital circuits, we can easily combine components into sophisticated systems that ultimately outperform those built from analog components in many applications
  digital -televisions, -cameras and -phones replace their analog predecessors
Digital systems represent information with discrete-valued variables
An early digital system:
  Charles Babbage’s Analytical Engine (1834-1871)
  use 25 gears with ten positions labelled 0 through 9
Electronic digital system use a binary representation (two-valued) in which a high voltage indicates a “1” and a low voltage indicates a “0” : bit ("binary digit”)
  why only two? It is easier to distinguish between two voltages than ten

## Slide 8: Digitalization (1)
The numeric representation x of a physical phenomenon over time is continuous x(t)
  at least at non-quantum scale
  e.g. temperature of a room, intensity of a light, force applied to an object, etc
The analog representation seems the most suitable and effective
Our abstraction needs a device able to convert continuous quantities variables into digital ones
  Analog to Digital Converters (ADC)
We need to digitize the signal both in time and in amplitude
  sampling and quantization

## Slide 9: Digitalization (2)

## Slide 10: Sampling
The reduction of a continuous-time signal to a discrete-time signal
  by measuring the value of the continuous function every T seconds
    sampling period T
    sampling frequency fs = 1/T (sample per second, hertz)
  sample: a value of the signal at a point in time
Which period T we need to use?

## Slide 11: Quantization
Mapping input values from a continuous set to output values in a finite number of elements
  rounding and truncation are typical examples
Quantization error
  difference between the input value and its quantized value
Resolution
  minute change in the input analog signal which changes the output digital signal

## Slide 12: Sensors
A device that produces an output signal for the purpose of sensing a physical phenomenon (like heat, pressure, humidity, movement, etc.)
  Example, light sensor: light sensitive resistors whose resistance decreases as the intensity of light they are exposed increases

## Slide 13: The amount of information
A set of S symbols and a word of length D, we can obtain SD distinct encodings
If we have a set of N objects that we want to encode, then SD >= N
In general, we know N and S and we want to find the minimum D >= logS N
The amount of information D of discrete variable (S=2) with N distinct states is measured in units of bits as:
  D = log2N [bits]
Examples:
  a binary variable has log22 = 1 bit of information
  to represent the 75 alphanumeric values (uppercase and lowercase characters, digits and special characters) we need a variable with 7 bits
    original ASCII (American Standard for Information Interchange) code was 7 bits
  a continuous signal theoretically contains an infinite amount of information because it can take on an infinite number of values
    in practice, noise and measurement error limit the information to only 10 to 16 bits for most continuous signals

## Slide 14: Boole Algebra
Digital signals may be treated with discrete math
If we limit to the case of only two values (the binary case), we can refer to the boolean algebra
The beauty of the digital abstraction is that digital designers can focus on 1 and 0, ignoring whether the boolean variables are physically represented with voltages, rotating gears, or even hydraulic fluid levels
  a computer programmer can work without needing to know the intimate details of the computer hardware
  on the other hand, understanding the details of the hardware allows the programmer to optimize the software better for that specific computer

## Slide 15: Exercises
Ex1.1: An analog voltage is in the range of 0–5V. If it can be measured with an accuracy of ±50 mV, at most how many bits of information does it convey?
  Solution: an accuracy of +/- 50mV indicates that the signal can be resolved to 100mV intervals. There are 50 such intervals in the range of 0-5V, so the signal represents log250 = 5.64 bits of information
Ex1.2: A classroom has an old clock on the wall whose minute hand broke off. (a) If you can read the hour hand to the nearest 15 minutes, how many bits of information does the clock convey about the time? (b) If you know whether it is before or after noon, how many additional bits of information do you know about the time?
  Solution: (a) the hour hand can be resolved to 12 * 4 = 48 positions, which represents log248 = 5.58 bits of information. (b) Knowing whether it is before or after noon adds one more bit