## Slide 1: Logic Gates and Circuits

## Slide 2: Index
Definition
NOT gate
BUFFER gate
AND gate
OR gate
XOR, NAND, NOR gates
Multiple inputs gates
Definition of digital circuits
Combinational or Sequential
Bus
Rules of combinational composition
Examples
Complexity

## Slide 3: Definition
Logic gates are simple digital circuits that take one or more binary inputs and produce a binary output
  drawn with a symbol showing the input and the output
  inputs are on the left (or top) and outputs on the right (or bottom)
The relationship between inputs and output is described with a truth table or a boolean equation
  a truth table lists inputs on the left and the corresponding output on the right, using one row for each possible combination of inputs
  a boolean equation is a mathematical expression using binary variables

## Slide 4: NOT gate
A NOT gate has one input, A, and one output, Y which is the inverse of the input
  If A is FALSE, then Y is TRUE
  If A is TRUE, then Y is FALSE
This relationship is summarized by the following truth table and boolean equation:
The line over A is pronounced NOT: “Y equals NOT A.”
The NOT gate is also called an inverter

## Slide 5: BUFFER gate
The other one-input logic gate is called a buffer: it simply copies the input to the output:
From the logical point of view, it is no different from a wire (it might seem useless)
From the analog point of view, the buffer might have desirable characteristics
  ability to deliver large amounts of current to a motor
  the ability to quickly send its output to many gates
We need to consider multiple levels of abstraction to fully understand a system; the digital abstraction hides the real purpose of a buffer.

## Slide 6: AND gate
The AND gate is a two-input logic gates that produces TRUE if and only if both inputs are TRUE; otherwise, the output is FALSE
The boolean equation can be written in several ways: Y=A•B, Y=AB, or Y=A∩B
  ∩ is pronounced “intersection” and it is preferred by logicians
  digital designers use Y=AB, read “Y equals A and B”

## Slide 7: OR gate
The OR gate produces TRUE if one input (or both) is TRUE
The boolean equation is written as Y=A+B or Y=A∪B
  ∪ symbol is pronounced “union” and is preferred by logicians
  digital designers normally use the + notation, pronounced “Y equals A or B.”

## Slide 8: XOR, NAND, NOR gates
Other common two-input logic gates are:
  XOR (exclusive OR, pronounced “ex-OR”) is TRUE if A or B, but not both, are TRUE
    it is indicated by ⊕, a plus sign with a circle around it.
  NAND gate performs NOT AND. Its output is TRUE unless both inputs are TRUE.
  NOR gate performs NOT OR. Its output is TRUE if neither A nor B is TRUE.

## Slide 9: Multiple inputs gates
Many boolean functions of three or more inputs exist:
  an N-input AND gate produces a TRUE output when all N inputs are TRUE
  An N-input OR gate produces a TRUE output when at least one input is TRUE

## Slide 10: Digital Circuit
In digital electronics, it is a network that processes discrete-valued variables
  a black box with one or more input terminals and one or more output terminals
  a functional specification describing the relationship between inputs and outputs
  a timing specification describing the delay between inputs changing and outputs responding
Inside the black box, circuits are composed of nodes and elements
  elements are circuits with inputs, outputs, and specifications
  nodes are wires, whose voltage conveys a discrete-valued variable
    input node receives values from the external world
    output node delivers values to the external world
    internal node not inputs or outputs

## Slide 11: Combinational or Sequential
Combinational circuit’s output depends only on the current values of the inputs
  combines the current input values to compute the output
  a logic gate is a combinational circuit
  memoryless
Sequential circuit’s output depends on both current and previous values of the inputs
  depends on the input sequence
  has memory
There are often many implementations for a single function
  we choose given the building blocks at our disposal and our design constraints (area, speed, power, etc).

## Slide 12: Bus
A bundle of multiple signals.
  a single line with a slash through it and a number next to it

## Slide 13: Rules of combinational composition
How we can build a large combinational circuit from smaller combinational circuit elements
A circuit is combinational if it consists of interconnected elements such that
  every element is itself combinational
  every node is either an input or connects to exactly one output of an element
  it contains no cyclic paths: every path through the circuit visits each at most once
The rules are sufficient but not necessary
  certain circuits that disobey these rules can be still combinational
  usually we restrict ourselves to combinational composition as a way to build combinational circuits

## Slide 14: Examples of circuits
It is combinational circuit
It is is not combinational
  there is a cyclic path
It is not combinational
  node n6 connects to the output of both I3 and I4
It is combinational
  two combinational circuits connected to form a larger combinational circuit
It does not obey the rules
  it has a cyclic path through the two elements
  depending on the functions of the elements, it may or may not be a combinational circuit

## Slide 15: Complexity
Large circuits such as microprocessors can be very complicated, so we use the principles to manage this complexity:
  view a circuit as a black box with a well-defined interface and function (abstraction and modularity)
  building the circuit out of smaller circuit elements (hierarchy)
  the rules of combinational (discipline)
The functional specification of a combinational circuit is usually expressed as a truth table or a boolean equation
  how to derive a boolean equation from any truth table?
  how to use boolean algebra to simplify equations?

## Slide 16: Exercises (1)
Ex3.1: Draw the symbol, boolean equation, and truth table for (a) a three-input OR gate; (b) a three-input exclusive OR (XOR) gate; (c) a four-input XNOR gate
  Solution:

## Slide 17: Exercises (2)
Ex3.2: Draw the symbol, boolean equation, and truth table for (a) a four-input OR gate; (b) a three-input XNOR gate
  Solution:

## Slide 18: Exercises (3)
Ex3.3: A majority gate produces a TRUE output if and only if more than half of its inputs are TRUE. Complete a truth table for a three-input majority gate.
  Solution:
Ex3.4: A three-input AND-OR gate produces a TRUE output if both A and B are TRUE or if C is TRUE. Complete a truth table for the gate.
  Solution: