## Slide 1: Boolean Algebra

## Slide 2: Index
Boolean Variable and Functions
Sum-of-Products and Product-of-Sums Forms
Axioms and Theorems
Derivation of the POS form
Perfect Induction
Simplifying Equations
Schematic
Programmable Logic Array
Drawing rules
Multiple-output circuits
Multilevel Combinational Logic
Bubble Pushing
X and Z
Karnaugh maps
Logic Minimization
Seven-segment Display Decoder
Don’t Cares

## Slide 3: Boolean Variable and Functions (1)
Let X be a certain discreet variable, we call boolean variable any discreet variable that can assume only two values:
  X = 0 False
  X = 1 True
If we have the boolean variables X1, X2, . . ., Xn
  f (X1, X2, . . . , Xn)
is called a boolean function, and it can assume only the values 0 and 1
  associates a boolean value to every element in its domain
The domain of a function of n-variables is composed of all the 2n combinations of their values
  domain’s elements are countable
Two functions are equivalent if they assume the same value for any combination of their variables’ values

## Slide 4: Boolean Variable and Functions (2)
The complement of a variable A is its inverse A
  we call A the true form of the variable
  and A the complementary form
Literals are the number of element that make up a boolean expression (not to be confused with the number of variables)
  f (a, b) is a logical function with two binary variables a and b
  f = a + b has 2 literals
  f = ab + ab has 4 literals
The AND of one or more literals is called implicant (or product)
  AB, ABC, and B are all implicants
A minterm is an implicant involving all the inputs to the function
  ABC is a minterm for a function of the three variables A, B, and C
The OR of one or more literals is called a sum
A maxterm is a sum involving all the inputs to the function
  A + B + C is a maxterm for a function of the three variables A, B, and C

## Slide 5: Boolean Variable and Functions (3)
The order of operations is important when interpreting equations
  NOT has the highest precedence
  followed by AND, then OR (just as in ordinary equations)
  Y = A + BC means Y = A OR (B AND C)

## Slide 6: Sum-of-Products Form (1)
A truth table of N inputs contains 2N rows
  one for each possible value of the inputs
We can associate each row with a minterm that is TRUE for that row
Example of two inputs:
  the minterm for the first row is A B because it is TRUE when A=0, B=0
The minterms are numbered starting with 0 (m0, m1, m2, and so on)
We can write the boolean equation by summing each of the minterms for which the output is TRUE
  in the example, there are two rows (or minterm) for which the output is TRUE
  thus, Y = A B + A B
This is called the sum-of-products (SOP) canonical form of a function, because it is the sum (OR) of products (AND). In sigma notation:
  f(A,B) = 𝛴(m1, m3)

## Slide 7: Sum-of-Products Form (2)
The sum-of-products form provides a boolean equation for any truth table with any number of variables:
  Y = A B C + A B C + A B C = 𝛴(m0,m4,m5)
Unfortunately, sum-of-products form does not necessarily generate the simplest equation
m0: A B C
m1: A B C
m2: A B C
m3: A B C
m4: A B C
m5: A B C
m6: A B C
m7: A B C

## Slide 8: Product-of-Sums Form (3)
An alternative way of expressing boolean functions
We can associate each row of a truth table with a maxterm that is FALSE for that row
Example of a two input:
  the maxterm for the first row is (A + B) it is FALSE when A=0, B=0
We can write the boolean equation as the AND of each of the maxterms for which the output is FALSE
  in the example, there are two maxterm for which the output Y is FALSE
  thus, Y = (A+B) (A+B)
This is called the product-of-sum (POS) canonical form of a function. In pi notation: f(A,B) = π(M0, M2)
SOP produces a shorter equation when the output is TRUE on only a few; POS is simpler when the output is FALSE on only a few rows

## Slide 9: Axioms
We learned how to write a boolean expression given a truth table
  that expression does not necessarily lead to the simplest set of logic gates
We can use boolean algebra to simplify boolean equations
  rules are much like those of ordinary algebra
  in some cases simpler, because variables have only two possible values
Based on a set of axioms that we assume as correct
  five axioms define boolean variables and the meanings of NOT, AND, and OR
  principle of duality: if the symbols 0 and 1 and the operators • (AND) and + (OR) are interchanged, the statement will still be correct

## Slide 10: Theorems of One Variable (1)
Describe how to simplify equations involving one variable:
T1 Identity theorem
  if one input of a two-input AND gate is always 1, we can remove the AND gate and replace it with a wire connected to the variable input
  if one input of a two-input OR gate is always 0, we can replace the OR gate with a wire connected to B
In general, gates cost money, power, and delay, so replacing it with a wire is beneficial!

## Slide 11: Theorems of One Variable (2)
T2 Null element theorem
  B AND 0 is always equal to 0 (null element for the AND operation because it nullifies the effect of any other input)
    if one input of an AND is 0, we can replace the AND with a wire that is tied LOW
  B OR 1 is always equal to 1 (null element for the OR operation)
    if one input of an OR is 1, we can replace the OR with a wire that is tied HIGH
T3 Idempotency theorem
  a variable AND/OR itself is equal to just itself
  idem (same) and potent (power)
  permits replacing a gate with a wire
T4 Involution theorem
  complementing a variable twice results in the original variable
  two inverters in series logically cancel each other out and are logically equivalent to a wire

## Slide 12: Theorems of One Variable (3)
T5 Complement theorem
  a variable AND its complement is 0
    because one of them has to be 0
  a variable OR its complement is 1
    because one of them has to be 1

## Slide 13: Theorems of Several Variables (1)
Describe how to simplify equations involving more than one variable:
T6 Commutativity and T7 Associativity theorems
  work the same as in traditional algebra
  the order of inputs does not affect the value of the output
  specific groupings of inputs do not affect the value of the output

## Slide 14: Theorems of Several Variables (2)
T8 Distributivity theorem
  AND distributes over OR and OR distributes over AND
  different from traditional algebra
    multiplication distributes over addition
    but addition does not distribute over multiplication ( (B + C) × (B + D) ≠ B + (C × D)
T9 Covering, T10 Combining, T11 Consensus theorems, T13 Absorption
  permit us to eliminate redundant variables
  prove true using other axioms and theorems:
    B•(B+C) = B•B + B•C = (T8 Distributivity) = B + B•C = (T3 Idempotency) = B•(1 + C) = (T8 Distributivity) = B•(1) = (T2 Null element) = B (T1 Identity)
    B•C + B•C = B•(C+C) = (T8Distributivity) = B•(1) = (T5’ Complements) = B (T1 Identity)
    B•C + B = (B+B) • (C+B)= (T8’ Distributivity) = (1) • (C+B) = (T5’ Complements) = C+B (T1 Identity)

## Slide 15: T12 De Morgan’s Theorem
The complement of the product of all the terms is equal to the sum of the complement of each term
  a NAND gate is equivalent to an OR gate with inverted inputs
The complement of the sum of all the terms is equal to the product of the complement of each term
  a NOR gate is equivalent to an AND gate with inverted inputs
The inversion circle is called a bubble
  intuitively, we can imagine that “pushing” a bubble through the gate causes it to come out at the other side and flips the body of the gate from AND to OR or vice versa

## Slide 16: Perfect induction
Proof of theorems with a finite number of variables are easy
  just show that the theorem holds for all possible values of these variables
Example: proving the T11 Consensus theorem using perfect induction:
  check both sides of the equation (BC + BD + CD = BC + BD) for all eight combinations of B, C, and D
  Because BC + BD + CD = BC + BD for all cases, the theorem is proved!

## Slide 17: Simplifying Equations (1)
Theorems help us simplify boolean equations
  example, consider the previously sum-of-products expression Y = AB + AB
  by using the T10 Combining theorem the equation simplifies to Y = B
  this may have been obvious looking at the truth table
  in general, multiple steps may be necessary to simplify more complex equations
The basic principle of simplifying sum-of-products equations is to combine terms using the relationship PA + PA = P, where P may be any term
How far can an equation be simplified?
  we define an equation in sum-of-products form to be minimized if it uses the fewest possible implicants
  if there are several equations with the same number of implicants, the minimal one is the one with the fewest literals
An implicant is called a prime implicant if it cannot be combined with any other implicants in the equation to form a new implicant with fewer literals
  implicants in a minimal equation must all be prime implicants
  otherwise, they could be combined to reduce the number of literals

## Slide 18: Simplifying Equations (2)
Minimize A B C + A B C + A B C
Minterms A B C and A B C differ only in A, so we can combine them to form B C
  B C + A B C
Notice that also minterms A B C and A B C differ by a single literal, thus we could have combined these two
  A B C + A B
Implicants B C and A B share the minterm A B C
So, are we stuck with simplifying only one of them?
Using the idempotency theorem, we can duplicate terms as many times
  T3 Idempotency: A B C + A B C + A B C +A B C
  T8 Distributivity: B C (A + A) + A B (C + C)
  T5 Complements: B C (1) + A B (1)
  T1 Identity: B C + A B

## Slide 19: Simplifying Equations (1)
Why bother simplifying a Boolean equation if it remains logically equivalent?
  reduction of the number of gates
  make the circuit smaller, cheaper, and possibly faster
Notice that simplifying boolean equations with theorems can take some trial and error, later we describes a methodical technique (Karnaugh maps) that makes the process easier

## Slide 20: Schematic
A schematic is a diagram of a digital circuit showing the elements and the wires that connect them
Notice that the simplified circuit has significantly less hardware than that of the original equation, it may be faster because it uses gates with fewer inputs

## Slide 21: Programmable Logic Array
Any Boolean equation in sum-of-products form can be drawn in a systematic way:
  draw columns for the inputs
  place inverters in adjacent columns
  draw rows of AND gates for each of the minterms
  for each output, draw an OR gate connected to the related minterms
This style is called a Programmable Logic Array (PLA) because the inverters, AND gates, and OR gates are arrayed in a systematic fashion

## Slide 22: Multiple-output Circuits
Many circuits have multiple outputs
  each computes a separate boolean function of the inputs
  we can write a separate truth table for each output
  or write all of the outputs on a single truth table
Example: priority circuit
  we can use sum-of-products form and reduce the equations using boolean algebra
  however, the simplified equations are clear by inspection
    notice that if A3 is 1, the outputs don’t care what the other inputs are: we use the symbol X
  Experienced designer often implement a logic circuit by inspection

## Slide 23: Multilevel Combinational Logic (1)
Logic in sum-of-products form is called two-level logic
  it consists of literals connected to a level of AND gates connected to a level of OR gates
  some logic functions require an enormous amount of hardware
Example: the XOR function of multiple variables
  consider building a three-input XOR using the two-level techniques
  an N-input XOR produces a TRUE output when an odd number of inputs are TRUE
  On the other hand, notice that:

## Slide 24: Multilevel Combinational Logic (2)
Designers often build circuits with more than two levels of logic gates
  may use less hardware
However, selecting the best multilevel implementation of a specific logic function is not a simple process: “best” has many meanings
  fewest gates, fastest, shortest design time, least cost, least power consumption, etc..
  “best” circuit in one technology is not necessarily the best in another
    e.g. CMOS circuits prefer NANDs and NORs over ANDs and ORs
With some experience, you will find that you can create a good multilevel design by inspection for most circuits
Computer-Aided Design (CAD) tools are also available to search a vast space of possible multilevel designs and seek the one that fits your constraints given the available building blocks

## Slide 25: Bubble Pushing
Redraw circuits (with lots of NAND and NOR) so that the function can be more easily determined
Algorithm:
  begin at the output of the circuit and work toward the inputs
  push bubbles back toward the inputs
    we can read the equation in terms of the output instead of its complement
  working backward, draw each gate in a form so that bubbles cancel
    If the current gate has an input bubble, draw the preceding gate with an output bubble
    bubbles in series cancel

## Slide 26: X and Z (1)
Boolean algebra is limited to 0 and 1, real circuits can also have illegal and floating values
X indicates that the circuit node has an unknown or illegal value
  commonly happens if it is being driven to both 0 and 1 at the same time
  this situation (contention) is considered to be an error and must be avoided
  the actual voltage on a node with may be somewhere between 0 and VDD, depending on the relative strengths of the gates driving gates
  X are also used by circuit simulator to indicate an uninitialized value
X can indicate “don’t care” values in truth tables
  be sure not to mix up the two meanings

## Slide 27: X and Z (2)
Z indicates that a node is being driven neither HIGH nor LOW
  the node is said to be floating or high impedance
Typical misconception: a floating node is the same as a logic 0. No: a floating node might be 0, might be 1, or might be at some voltage in between
A common way to produce a floating node is to forget to connect a voltage to a circuit input
  this may cause the circuit to behave erratically, as the floating input randomly changes from 0 to 1
  touching the circuit may be enough to trigger the change by means of static electricity from the body
  you can seen circuits that operate correctly only as long as the student keeps a finger pressed on a chip…

## Slide 28: Karnaugh maps
K-maps are a graphical method for simplifying boolean equations
  works well for problems with up to four variables
  give insight into manipulating boolean equations
  invented in 1953 by Maurice Karnaugh, a telecommunications engineer at Bell Labs
Recall that logic minimization involves combining terms
  two terms containing an implicant P and the true and complementary forms of some variable A are combined to eliminate A:
    PA + PA = P
  Karnaugh maps make these combinable terms easy to see by putting them next to each other in a grid

## Slide 29: Constructing a Map (1)
Consider the truth table of a three-input function:
The K-map of that table is constructed as:
  top row gives the four possible values for A and B
  left column gives the two possible values for C
  each square corresponds to a row in the truth table and contains the value of the output
    a single minterm
  For example:
    top left square corresponds to the first row in the truth table Y 1 when ABC=000
    the minterm is A B C

## Slide 30: Constructing a Map (2)
Notice that, each square (minterm) differs from an adjacent square by a change in a single variable
  adjacent squares share all the same literals except one
  which appears in true form in one square and in complementary form in the other
    squares representing the minterms A B C and A B C are adjacent and differ only in the variable C
In order to obtain this property, A and B combinations in the top row are in a peculiar order (Gray code)
  00, 01, 11, 10
  differs from ordinary binary order (00, 01, 10, 11) in that adjacent entries differ only in a single variable
The K-map also “wraps around”
  squares on the far right are “adjacent” to the squares on the far left
    they differ only in one variable (A)
  we can roll the map into a cylinder form a torus

## Slide 31: Constructing a Map (3)
We can use boolean algebra to minimize equations in sum-of-products form:
However, K-maps help us do this simplification graphically:
  circle all the rectangular blocks of 1 in the map
    each circle should be as large as possible
  for each circle, write the corresponding implicant
    variables whose true and complementary forms are both in the circle are excluded from the implicant
  In the example:
    C has both its true form and its complementary form (0) in the circle, so we do not include it in the implicant
    Y is TRUE when A=B=0, independent of C
The K-map gives the same answer we reached using boolean algebra

## Slide 32: Logic Minimization with K-Maps
More formally, recall that a boolean equation is minimized when it is written as a sum of the fewest number of prime implicants
  each circle on the K-map represents an implicant
  the largest possible circles are prime implicants
Rules for finding a minimized equation from a K-map are as follows:
  all the squares in each circle must contain 1
  use the fewest circles necessary to cover all the 1
  each circle must span a rectangular block that is a power of 2 (i.e. 1, 2, or 4) squares in each direction
  each circle should be as large as possible
  a circle may wrap around the edges of the K-map
  a 1 in a K-map may be circled multiple times if doing so allows fewer circles to be used

## Slide 33: Example of minimization
Suppose we have the function Y = F(A, B, C) with the following K-map:
Minimize the equation:
  circle the 1 using as few circles as possible
  form the prime implicant by writing those variables that appear in the circle only in true or only in complementary form
Notice
  the top-right square is covered twice to make the prime implicant circles as large as possible
  the circle covering four squares wraps around the sides of the K-map

## Slide 34: Seven-segment Display Decoder (1)
A device that takes a 4-bit data input D3:0 and produces seven outputs Sa - Sg to control a display from 0 to 9
The truth table is:

## Slide 35: Seven-segment Display Decoder (2)
Each of the seven outputs is an independent function of four variables
As an example, we can draws K-maps for outputs Sa and Sb
  Remember to label rows and columns in Gray code order: 00, 01, 11, 10

## Slide 36: Seven-segment Display Decoder (3)
Circle the prime implicants:
Notice that the minimal set of prime implicants is not unique
For example
  0000 entry in the Sa K-map was circled along with the 1000 entry to produce the D2 D1 D0 minterm
  the circle could have included the 0010 entry instead, producing a D3 D2 D0 minterm

## Slide 37: Don’t Cares (1)
Recall that “don’t care” entries for truth table inputs
  can reduce the number of rows in the table when some variables do not affect the output
  hey are indicated by the symbol X, which means that the entry can be either 0 or 1
Don’t cares also appear in truth table outputs where
  the output value is unimportant
  or the corresponding input combination can never happen
  such outputs can be treated as either 0’s or 1’s at the designer’s discretion
In a K-map, X’s allow for even more logic minimization
  they can be circled if they help cover the 1 with fewer or larger circles,
  but they do not have to be circled if they are not helpful

## Slide 38: Don’t Cares (2)
We can review the seven-segment display decoder if we don’t care about the output values for illegal input values of 10 to 15
Because don’t cares can be 0 or 1, we circle a don’t care if it allows us to cover the 1 with fewer or bigger circles
Use of don’t cares simplifies the logic substantially

## Slide 39: Exercises (1)
Ex5.1: Write a Boolean equation in sum-of-products canonical form for each of the truth tables
  Solution:

## Slide 40: Exercises (2)
Ex5.2: Write a Boolean equation in product-of-sums canonical form for each of the truth tables
  Solution:

## Slide 41: Exercises (3)
Ex5.3: Sketch a reasonably simple combinational circuit implementing each of the following functions. Reasonably simple means that you are not wasteful of gates, but you don’t waste vast amounts of time checking every possible implementation of the circuit either.
  Solution:

## Slide 42: Exercises (4)
Ex5.4: Find a minimal Boolean equation for the following true table and sketch the circuit
  Solution:

## Slide 43: Exercises (5)
Ex5.5: Find a minimal Boolean equation for the following true table and sketch the circuit
  Solution:

## Slide 44: Exercises (6)
Ex5.6: Complete the design of the seven-segment decoder segments Sc through Sg and sketch a reasonably simple gate-level implementation of part
  Solution: