## Slide 1: Beneath the abstraction

## Slide 2: Index
Relate the continuous to discrete
  Logic Level
  Noise Margins
  DC Transfer Characteristics
  Logic families
Implementing Logic Gates
  Gears and vacuum tubes
  The Revolution of Integration
  Moore Law
Electron devices
  Silicon
  Semiconductors
  p-n junction
  Diode
  MOS Transistors
Logic gates from transistor
  NOT, NAND, NOR

## Slide 3: Relate the continuous to discrete
A digital system uses discrete-valued variables
However, the variables are represented by continuous physical quantities
  the voltage on a wire, the position of a gear, or the level of fluid in a cylinder
The designer must choose a way to relate the continuous value to the discrete value
Consider representing a binary signal A with a voltage on a wire
  let 0 volts (V) indicate A=0 and 5V indicate A=1
  any real system must tolerate some noise
    so 4.97V probably can to be interpreted as A=1 as well
    but what about 4.3V? or 2.8V? or 2.5V?

## Slide 4: Logic Level and Noise Margins (1)
The lowest voltage is 0V, also called ground or GND
The highest voltage comes from the power supply and is called VDD
The mapping is done by defining logic levels
The noise margins are the amount of noise that could be added to an output such that the signal can still be interpreted as a valid input
  NML = VIL – VOL, NMH = VOH – VIH

## Slide 5: Logic Level and Noise Margins (2)
Consider the following circuit:
  VO1 is the output voltage of inverter I1
  VI2 is the input voltage of inverter I2
Both inverters have the following characteristics
  VDD=5V, VIL=1.35V, VIH=3.15V, VOL=0.33V, VOH=3.84V
What are the inverter low and high noise margins?
  NML = VIL – VOL = 1.35V − 0.33V = 1.02V
  NMH = VOH − VIH = 3.84V − 3.15V = 0.69V
Can the circuit tolerate 1V of noise between VO1 and VI2?
  it can tolerate the noise when the output is LOW (NML = 1.02 V)
  but not when the output is HIGH (NMH = 0.69V)
How can we define those values?

## Slide 6: DC Transfer Characteristics
The output voltage as a function of the input voltage
To understand the limits of the digital abstraction, we must delve into the analog behaviour of a gate

## Slide 7: Logic families
Static discipline: if inputs are logically valid, outputs will also be valid
  ensures simplicity, robustness, and scalability
  like a grammar: valid “words” (gates) → valid “sentences” (circuits)
Gates must use compatible logic levels → grouped into logic families
Compatibility:
  within a family: gates ”snap together” like Lego
  across families requires caution or interfacing
Trend: shift from 5V → 3.3V → 2.5V → 1.8V → lower for reduced power

## Slide 8: Implementing Logic Gates
How can we implement logic gates?
  Bbabbage’s Analytical Engine was built from gears
  early electrical computers used vacuum tubes
What’s the problem? → large, fragile, power-hungry, and unreliable

## Slide 9: The Revolution of Integration
Modern digital systems use transistors
  electrically controlled switches that turn ON or OFF when a voltage or current is applied to a control terminal
  cheap, small, and reliable
Revolution: the ability to integrate large numbers of transistors onto a single chip
  1958, Jack Kilby at Texas Instruments built the first integrated circuit
  1959: Robert Noyce at Fairchild Semiconductor patented a method for interconnecting multiple transistors on a single silicon chip
  at the time, transistors cost about $10 each; after some decades of advances, we can pack roughly one billion MOS onto a 1 cm2 chip of silicon, and each transistor cost less than 10 micro-cents

## Slide 10: Moore Law
The number of transistors on an integrated circuit was doubling roughly every two years.

## Slide 11: Transistor scaling

## Slide 12: Beyond Moore
Exponential growth in transistor counts drove higher speed, memory, and lower cost → fuelled the Information Age
Scaling is slowing (last decade)
  atomic-scale barriers (quantum effects, heat, manufacturing, materials)
Strategies Beyond Scaling:
  Multi-core processors → parallelism instead of faster clocks
  3D integration → stacking circuits to reduce delay and increase density
New paradigms:
  New materials (graphene, nanotubes, 2D semiconductors)
  Specialized accelerators (GPUs, AI chips)
  Quantum computing → beyond classical logic

## Slide 13: Silicon
Modern transistors use MOS technology based on silicon (Si)
Silicon has 4 valence electrons, forming covalent bonds → stable crystal lattice
  Pure silicon = poor conductor (no free carriers)
Doping: tuning conductivity
  n-type (e.g. As) → extra electron → free negative charge
  p-type (e.g. B) → missing electron → hole behaves like positive charge
➡️ By adjusting dopants, silicon’s conductivity can vary over many orders of magnitude → basis for diodes and transistors

## Slide 14: Semiconductor
Doping: tuning conductivity
  n-type (e.g. As) → extra electron → free negative charge
  p-type (e.g. B) → missing electron → hole behaves like positive charge
➡️ By adjusting dopants, silicon’s conductivity can vary over many orders of magnitude → basis for diodes and transistors

## Slide 15: p-n junction (1)

## Slide 16: p-n junction (2)

## Slide 17: Diode

## Slide 18: MOS Transistors (1)
MOSFET (Metal–Oxide–Semiconductor Field-Effect Transistor) is a sandwich of several layers of conducting and insulating materials:
MOS behaves as a voltage-controlled switch in which the gate voltage creates an electric field that turns ON or OFF a connection between the source and drain

## Slide 19: MOS Transistors (2)
Consider the nMOS:
pMOS works in just the opposite fashion
  the substrate is tied to Vdd
  when the gate is also at VDD, the pMOS is OFF
  when the gate is at GND, the channel inverts to p-type and the transistor is ON

## Slide 20: Switch models of MOS
CMOS give us two types of electrically controlled switches
Gate regulates current between source and drain
  nMOS are OFF when the gate is 0 and ON when the gate is 1
  pMOS are just the opposite
Unfortunately, MOS are not perfect switches
  nMOS transistors pass 0 well, but pass 1 poorly
  pMOS transistors pass 1 well, but 0 poorly

## Slide 21: CMOS
To build digital logic efficiently, both nMOS and pMOS transistors must be fabricated on the same chip
Complementary MOS or CMOS

## Slide 22: CMOS
To build digital logic efficiently, both nMOS and pMOS transistors must be fabricated on the same chip
Complementary MOS or CMOS

## Slide 23: Building Integrated Circuits

## Slide 24: CMOS gates
NOT
NAND
NOR
Transmission Gate

## Slide 25: Power consumption
The amount of energy used per unit time
Battery life of portable systems
  a smartphone battery holds about 10 W-hr of energy, meaning that it could deliver 1W for 10 hours or 2W for 5 hours, and so forth
  for your phone to last a full day, its average consumption should be under 1W
  laptops typically have 50 to 100 W-hr batteries and consume under 10W in normal operation, of which the screen is a large fraction
Power is also significant for plugged systems
  electricity costs money and emissions
  the system will overheat if it draws too much power
Digital systems draw both dynamic and static power
  dynamic: power used as signals change between 0 and 1
  static: power used even when signals do not change, and the system is idle