## Slide 1: Number Systems

## Slide 2: Index
Decimal Numbers
Binary Numbers
Hexadecimal Numbers
Bytes
Kilo, Mega and Giga
Binary arithmetic
Two’s complement format
Fractional Numbers
Fixed-Point Number Systems
Floating-Point Number Systems

## Slide 3: Decimal Numbers
In elementary school, we learned to do arithmetic in decimal
  just as we have ten fingers, there are ten decimal
  digits: 0, 1, 2, …, 9
Decimal digits are joined together to form longer decimal numbers
  each column of a decimal number has ten times the weight of the previous column
  from right to left, the column weights are 1, 10, 100, 1000, and so on
Decimal numbers are referred to as base 10
An N-digit decimal number represents one of 10N possibilities
  range of the number
  a three-digit decimal number represents one of 1000 possibilities in the range 0 to 999

## Slide 4: Binary Numbers
Bits (binary digit) represent one of two values, 0 or 1, and are joined together to form binary numbers
  a column of a binary number has twice the weight of the previous column (base 2)
  column weights are 1, 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, 4096, 8192, 16384, 32768, 65536
An N-bit number represents one of 2N possibilities

## Slide 5: Decimal to binary conversion
Convert the decimal number 8410 to binary
Working from the left:
  1, 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, 4096, 8192, 16384, 32768, 65536
  the largest power of 2 less than or equal to 84 is 64, so there is a 1 in the column 7, leaving 84 − 64 = 20; 20 < 32, so there is a 0 in column 6; 20 ≥ 16, so there is 1 in the column 5, leaving 20 − 16 = 4; 4 < 8, so there is 0 in column 4; 4 ≥ 4, so there is 1 in column 3, leaving 4 − 4 = 0; thus, there must be 0 in columns 2 and . Putting all together, 8410 = 10101002
Working from the right:
  repeatedly divide the number by 2. The remainder goes in each column
  84/2 = 42, so 0 goes in column 1; 42/2 = 21, so 0 goes in column 2; 21/2 = 10 with the remainder of 1 going in column 3; 10/2 = 5, so 0 goes in column 4; 5/2 = 2 with the remainder of 1 going in column 5; 2/2 = 1, so 0 goes column 6. Finally, 1/2 = 0 with the remainder of 1 going in column 7. Again, 8410 = 10101002

## Slide 6: Hexadecimal Numbers
Writing long binary numbers becomes tedious and prone to error
A group of four bits represents one of 24 = 16 possibilities
  it is convenient to work in base 16, called hexadecimal
  use the digits 0 to 9 along with the letters A to F
Conversion between hexadecimal and binary is easy because each hexadecimal digit directly corresponds to four binary digits
  convert 2ED16 to binary
    216 = 00102, E16 = 11102, D16 = 11012, so 2ED16 = 0010 1110 11012
  convert 11110102 to hexadecimal
    10102 = A16, 1112 = 716, so 11110102 = 7A16

## Slide 7: Bytes
A group of eight bits is called byte
  it represents one of 28 = 256 possibilities
  size of objects stored in memories is measured in bytes rather than bits
A group of four bits is called nibble
  it represents one of 24 = 16 possibilities
  an hexadecimal digit stores one nibble
  no longer a commonly used unit
Microprocessors handle data in chunks called words
  the size of a word depends on the architecture of the microprocessor
  most computers had 64-bit processors, indicating that they operate on 64-bit words, older computers handling 32-bit words were also widely available
Within a group of bits…
  …the bit in the first column (on the right) is called the least significant bit (lsb)
  …the bit at the other end (on the left) is called the most significant bit (msb),
Similarly, within a word: the bytes are identified as least significant byte (LSB) through most significant byte (MSB)

## Slide 8: Kilo, Mega and Giga
By coincidence, 210 = 1024 ≈ 103, so, the term kilo indicates 210
  210 bytes is one 1 KB
Similarly, mega (million) indicates 220 ≈ 106, and giga (billion) indicates 230 ≈ 109
Using these approximation and remembering the powers of two up to 29, it is easy to estimate any power of two
  1, 2, 4, 8, 16, 32, 64, 128, 256, 512
  find the approximate value of 224 without using a calculator
    split the exponent into a multiple of ten and the remainder
    224 = 220 × 24; 220 ≈ 1 million; 24 = 16; so 224 ≈ 16 million (16,777,216, close enough)

## Slide 9: Binary Addition
Like decimal addition, but easier
  if the sum of two numbers is greater than what fits in a single digit (1), we carry a 1 into the next column (carry bit)
We operate on a fixed number of digits, so additions can overflow
  if the result is too big to fit in the available digits
    a 4-bit number has the range [0, 15], an addition overflows if the result exceeds
    the fifth bit is discarded, producing an incorrect result in the remaining four bits
  this can be detected by checking for a carry out of the most significant column

## Slide 10: Signed Binary Numbers
We need to represent also negative numbers
Sign/magnitude
  use the most significant bit as the sign and the remaining N − 1 bits as the magnitude (absolute value): a sign bit of 0 indicates positive and a sign bit of 1 indicates negative
  intuitively appealing: match our way of writing negative numbers with a minus sign followed by the magnitude
  ordinary binary addition does not work
    −510 + 510 gives 11012 + 01012 = 100102, which is nonsense
  It is odd that both +0 and −0 exist, both indicate zero…
Two’s complement
  identical to unsigned binary numbers except that the most significant bit has a weight of −2N−1 (instead of 2N−1)
  this overcomes the shortcomings of sign/magnitude numbers
    zero has a single representation
    ordinary addition works

## Slide 11: Two’s complement representation
Zero is written as all zeros
  00…0002
The most positive number has a 0 in the msb and 1 elsewhere
  01…1112 = 2N−1 − 1
The most negative number has a 1 in the msb and 0 elsewhere
  10…0002 = −2N−1
−1 is written as all ones:
  11…1112
Notice that the most significant bit can be viewed as the sign bit

## Slide 12: Two’s complement negative number
The sign of a two’s complement number is reversed by inverting the bits in the number (called one’s complement) and then adding 1
  reversing the sign
Find the representation of −210 as a 4-bit two’s complement number
  represent the magnitude: +210 = 00102
  invert 00102 to 11012
  add 1: 11012 + 12 = 11102
  so, −210 is 11102
Find the decimal value of the 4-bit two’s complement number 10012
  10012 has a leading 1, so it must be negative
  Invert the magnitude 10012 = 01102
  add 1: 01102 + 12 = 01112 = 710
  so, 10012 = −710

## Slide 13: Addition and Subtraction
Addition works properly for both positive and negative numbers
  recall: when adding N-bit numbers, the carry of the Nth bit is discarded
  compute −210 + 110 and −710 + 710 using 4-bit two’s complement numbers
    −210 + 110 = 11102 + 00012 = 11112 = −110
    −710 + 710 = 10012 + 01112 = 100002, the fifth bit is discarded, leaving 00002
Subtraction is performed by taking the two’s complement of the second number, then adding
  compute 510 − 310 and 310 − 510 using 4-bit two’s complement numbers
    310 = 00112, take its two’s complement −310 = 11012, then add 510 + (−310) = 01012 + 11012 = 00102 = 210 notice that the carry of the most significant position is discarded because the result is stored in four bits
    take the two’s complement of 510 to obtain −510 = 10112, add 310 + (−510) = 00112 + 10112 = 11102 = −210

## Slide 14: Zero
The two’s complement of 0 is found by inverting all the bits (11…1112) and adding 1, which produces all 0’s, disregarding the carry out of the msb
  zero is always represented with all 0’s
  unlike the sign/magnitude system, it has no separate -0 representation
  zero is considered positive because its sign bit is 0
The range of an N-bit two’s complement number spans [−2N−1, 2N−1 − 1]
  there is one more negative number than positive number because there is no −0
The most negative number 10…0002 = −2N−1 is called the weird number
  its two’s complement is found by inverting the bits (01…1112) and adding 1, which produces 10…0002, the weird number again.
  it has no positive counterpart

## Slide 15: Overflow
Adding two N-bit positive numbers or negative numbers may cause overflow
  if the result is greater than 2N−1 − 1 or less than −2N−1
  unlike unsigned numbers, a carry out of the most significant column does not indicate overflow
Overflow occurs if the two numbers have the same sign bit and the result has the opposite sign bit
  Compute 410 + 510 using 4-bit two’s complement numbers
    410 + 510 = 01002 + 01012 = 10012 = −710
    the result overflows, producing an incorrect negative result
    if the computation had been done using five bits, the result 010012 = 910 would have been correct

## Slide 16: Sign extension
When a two’s complement number is extended to more bits, the sign bit must be copied into the most significant bit positions
  this process is called sign extension
For example:
  310 and −310 are written as 4-bit two’s complement numbers 00112 and 11012
  a sign-extension to seven bits is 00000112 and 11111012

## Slide 17: Multiplication
Multiplication of unsigned binary numbers is similar to decimal multiplication but involves only 1 and 0
  partial products are formed by multiplying a single digit of the multiplier with the entire multiplicand
  the shifted partial products are summed to form the result
  partial products in the binary case are either the multiplicand or all 0

## Slide 18: Comparison

## Slide 19: Fractional Numbers
Computers operate on both integers and fractions
  we have only considered representing signed or unsigned integers
  fixed- and floating-point number systems that can represent rational numbers
Fixed-point numbers are analogous to decimals
  some of the bits represent the integer part, and the rest represent the fraction
Floating-point numbers are analogous to scientific notation
  with a mantissa and an exponent

## Slide 20: Fixed-Point Number Systems (1)
It has an implied binary point between the integer and fraction bits
  analogous to the point between the integer and fraction digits of a decimal number
  0110.1100 = 22+21+2-1+2-2 = 6.75
Signed fixed-point numbers can use either
  sign/magnitude notation
    the most significant bit is used to indicate the sign
    -2.37510 = 1010.01102
  two’s complement
    inverting the bits of and adding a 1 to the least significant (rightmost) bit
    -2.37510 = 1101.10102
Like all binary number representations, fixed-point numbers are just a collection of bits
  there is no way of knowing the existence of the binary point
  only through agreement of those people interpreting the number

## Slide 21: Fixed-Point Number Systems (2)
We use
  Ua.b to denote an unsigned fixed-point number with a integer bits and b fraction bits;
  Qa.b to denote a signed (two’s complement) fixed point number with a integer bits (including the sign bit) and b fractional bits
Fixed-point number systems are commonly used in digital signal processing (DSP), graphics, and machine learning application
  Q1.15 (also known as Q15) is the most common format, storing signed numbers in the range (−1, 1) with 15 bits of precision
  Q1.31 (also called just Q31) is sometimes used for higher precision intermediate results such as in a Fast Fourier Transform
  U8.8 is sometimes used for sensor readings sampled by analog/digital converters (ADCs)
Note that all formats pack into 16- or 32-bit words for efficient storage in computer memories

## Slide 22: Floating-Point Number Systems (1)
Analogous to scientific notation
  have a sign, mantissa (M), base (B), and exponent (E)
    ± M * BE
    4.1*103 is the scientific notation for 4100 (mantissa 4.1, base 10, and exponent 3)
    the decimal point “floats" to the position right after the most significant digit.
  allowing the representation of very large and very small number
32-bit floating-point numbers
  base 2, 1 sign bit, 8 exponent bits, and 23 mantissa bits
  22810 = 111001002 = 1.11001*27 = 1.11001*200000111
Notice that the first bit of the mantissa is always 1 and therefore need not be stored (implicit leading one)
  this frees up an extra bit for useful data

## Slide 23: Floating-Point Number Systems (2)
The exponent needs to represent both positive and negative exponents
  use a biased exponent, which is the original exponent plus a constant bias
  32-bit floating-point uses a bias of 127
    exponent 7 is biased 7 + 127 = 134 = 100001102
    exponent −4 is biased −4 + 127 = 123 = 011110112
This notation conforms to the IEEE 754 floating-point standard
  22810 = 111001002 = 1.11001*210000110
The standard has special cases to represent zero, infinity, and illegal results

## Slide 24: Floating-Point Number Systems (3)
So far, we have examined 32-bit floating-point numbers
  single-precision (float)
The IEEE 754 standard also defines
  64-bit double-precision numbers (doubles)
  128-bit quadruple-precision numbers (quads)
    not yet widely supported in hardware
    or software.

## Slide 25: Exercises (1)
Ex2.1: The Babylonians developed the sexagesimal (base 60) number system about 4000 years ago. How many bits of information is conveyed with one sexagesimal digit? How do you write the number 400010 in sexagesimal?
  Solution: each digit conveys log260 = 5.91 bits of information. 400010 = 1 6 4060 (1 in the 3600 column, 6 in the column 60, and 40 in the column 1)
Ex2.2: How many different numbers can be represented with 16 bits?
  Solution: 216 = 65.536 numbers
Ex2.3: What is the largest unsigned 32-bit binary number?
  Solution: 232-1 = 4.294.967.295
Ex2.4: What is the largest 16-bit binary number that can be represented with (a) unsigned numbers? (b) two’s complement numbers? (c) sign/magnitude numbers?
  Solution: (a) 216-1=65.535; (b) 215-1=32.767; (c) 215-1=32.767

## Slide 26: Exercises (2)
Ex2.5: Convert the following unsigned binary numbers to decimal and to hexadecimal: (a) 10102; (b) 1101102; (c) 111100002; (d) 0001000101001112
  Solution: (a) 10, (b) 54, (c) 240, (d) 2215; (a) A, (b) 36, (c) F0, (d) 8A7
Ex2.6: Convert the following hexadecimal numbers to decimal: (a) A516; (b) 3B16; (c) FFFF16, (d) D000000016
  Solution: (a) 165; (b) 59; (c) 65.535; (d) 3.489.660.928
Ex2.7: Convert the following two’s complement binary numbers to decimal: (a) 10102; (b) 1101102; (c) 011100002; (d) 100111112
  Solution: (a) -6; (b) -10; (c) 112; (d) -97
Ex2.8: Convert the following decimal numbers to 8-bit two’s complement numbers or indicate that the decimal number would overflow the range: (a) 4210; (b) −6310; (c) 12410; (d) −12810; (e) 13310
  Solution: (a) 00101010; (b) 11000001; (c) 01111100; (d) 10000000; (e) overflow