## Slide 1: Combinational Building Blocks

## Slide 2: Index
Building Blocks
Multiplexer
Decoders
Adders
Subtractor
Comparators
Arithmetic/Logical Unit (ALU)
Shifters and Rotators
Multiplier and divider
Floating-Point Addition

## Slide 3: Building Blocks
Combinational logic is often grouped into larger building blocks to build more complex systems
  principles of abstraction, hierarchy, modularity, and regularity
  hiding the unnecessary gate-level details to emphasize the function of the building block
  hierarchically assembled from simpler components
  a well-defined interface and can be treated as a black box
Examples:
  seven-segment display decoders (already considered)
  multiplexers
  decoders
  arithmetic circuits
We will use many of these building blocks to build a microprocessor

## Slide 4: Multiplexer (mux)
A device that choose an output among several possible inputs, based on the value of a select signal
A 2:1 multiplexer has two data inputs and one output and a select signals
  if S=0, Y=D0,
  if S=1, Y=D1

## Slide 5: Wider multiplexer
A 4:1 multiplexer has four data inputs and one output and two select signals are needed to choose among the four data inputs
  it can be built using sum-of-product logic, or multiple 2:1 multiplexers
Wider multiplexers (8:1 and 16:1) can be built by expanding the method
  in general, an N:1 multiplexer needs log2N select lines

## Slide 6: Multiplexer Logic (1)
Multiplexers can be used as lookup tables to perform logic functions
For example, we can use a multiplexer to implement a two-input AND gate
  A and B serve as select lines
  inputs are connected to 0 or 1, according to the corresponding row of the truth table
  changing the data inputs, the multiplexer can be reprogrammed to perform a different function
In general, a 2N-input multiplexer can be programmed to perform any N-input logic function by applying 0 and 1 to the appropriate data inputs
We can also cut the multiplexer size in half, using only a 2N–1-input multiplexer to perform any N-input logic function
  provide one of the literals to the multiplexer inputs:

## Slide 7: Multiplexer Logic (2)
As an example, implement the following function using a 8:1 multiplexer and a 4:1 multiplexer:

## Slide 8: Decoders
A device with N inputs and 2N outputs that asserts exactly one of its outputs depending on the input combination
For example, consider a 2:4 decoder
  when A1:0 = 00, Y0 is 1
  when A1:0 = 01, Y1 is 1
  and so forth
The outputs are called one-hot
  because exactly one is “hot” (HIGH) at a given time
In the implementation, each gate depends on either the true or the complementary form of each input
  an N:2N decoder can be constructed from 2N N-input AND gates that accept the various combinations of true or complementary inputs
  each output in a decoder represents a single minterm
    for example, Y0 represents the minterm A1 A0.

## Slide 9: Decoder Logic
Decoders can be combined with OR gates to build logic functions
  because each output of a decoder represents a single minterm, the function is built as the OR of all of the minterms in the function
  example: a two-input XNOR function using a 2:4 decoder and a single OR gate
An N-input function with M 1’s in the truth table can be built with an N:2N decoder and an M-input OR.
This concept will be applied to the building of read-only memories (ROMs)

## Slide 10: Half and Full Adders
Addition is one of the most common operations in digital systems
Half adder
  two inputs, A and B, and two outputs, S and Cout
  S is the sum of A and B
  C is the eventual carry out
In a multi-bit adder, Cout is added (carried) in to the next most significant bit
  half adder lacks a Cin input to accept the Cout of the previous column.
Full Adder
  accepts also the carry in Cin

## Slide 11: Carry Propagate Adder
A N-bit adder that sums two N-bit inputs and a carry in to produce an N-bit result S and a carry out
  the carry out of one bit propagates into the next bit
  drawn like a full adder except that input/output are busses rather than single bits
The simplest way to build it is to chain together N full adders
  Cout of one stage acts as the Cin of the next stage
  Ripple-Carry Adder
A good application of modularity and regularity
  full adder module is reused many times to form a larger system
It is slow when N is large.
  S31 depends on C30, which depends on C29, and so forth
  the delay of the adder triple = N * tFA grows directly with the number of bits

## Slide 12: Carry-Lookahead Adder (1)
Ripple-Carry Adders are slow because the carry must propagate
We can divide the adder into blocks and determine the carry out of a block as soon as the carry in is known
  it looks ahead across the blocks rather than wait to ripple through all the full adders
CLA use generate (G) and propagate (P) signals
  a column i “generates” a carry if it produces a carry independent of the carry in
    both input are 1: Gi = Ai AND Bi
  a column i “propagates” a carry if it produces a carry whenever there is a carry in
    either one of the input is 1: Pi = Ai OR Bi
Using this definition, a column i will generate a carry out if it either generates or propagates a carry:
  Ci = Gi + Pi Ci-1 = Ai Bi + (Ai + Bi) Ci-1

## Slide 13: Carry-Lookahead Adder (2)
We can extend to multiple-bit blocks
  a block “generates” a carry if it produces a carry out independent of the carry in
  a block “propagate” a carry if it produces a carry out whenever there is a carry in
We define block generate and propagate signals
  Gi:j and Pi:j for blocks spanning columns i through j
A block generates a carry…
  …if the most significant column generates a carry
  …if the previous column generated a carry and the most significant column propagates it, and so forth
  G3:0 = G3 + P3(G2 + P2(G1 + P1G0)
A block propagates a carry….
  if all the columns in the block propagate the carry
  P3:0 = P3P2P1P0
We can quickly compute the carry out of the block i
  Ci = Gi:j + Pi:jCj-1

## Slide 14: Carry-Lookahead Adder (2)
A 32-bit carry-lookahead adder composed of eight 4-bit blocks
Each block contains a 4-bit ripple-carry adder and lookahead logic to compute the carry out of the block given the carry in
Logic gates needed to compute the column generate and propagate signals, Gi and Pi , using signals Ai and Bi

## Slide 15: Carry-Lookahead Adder (3)
All blocks compute column generate and propagate signals simultaneously
Then Cin advances directly to Cout through each block until the last
  Cin proceeds through the lookahead gates to produce C3
  C3 proceeds through its lookahead block to produce C7
  C7 proceeds through its lookahead block to produce C11
  and so on until C27, the carry in to the last block
  finally, the last block contains a short ripple-carry adder (no more the lookahead logic)
An N-bit adder divided into k-bit blocks has a delay
  tCLA = tpg + tpg_block + (N/k -1) tlookahead + k tFA
    tpg is the delay to generate signals Pi and Gi
    tpg_block is the delay to to generate signals Pi:j and Gi:j for a k-bit block
    tlookahead is the delay from Cin to Cout through the logic of the k-bit CLA block
For N > 16, the carry-lookahead adder is much faster than the ripple-carry adder
  however, the adder delay still increases linearly with N

## Slide 16: Ripple-Carry Adder vs Carry-Lookahead Adder
Compare the delays of a 32-bit ripple-carry adder and a 32-bit carry-lookahead adder with 4-bit blocks
Assume that each gate delay is 100ps and that a full adder delay is 300ps
The propagation delay of the 32-bit ripple-carry adder is
  triple = N * TFA = 32 * 300ps = 9.6 ns
The carry-lookahead adder has
  tpg = 100ps (one AND or one OR)
  tpg_block = 6 * 100 ps = 600ps (six AND/OR gates)
  tlookahead = 2 * 100 ps = 200ps (one OR and one AND)
  tCLA=tpg+tpg_block+(N/k-1)tlookahead+ktFA = 100 + 600 + (32/4 - 1)*200 + 4*300 = 3.3ns
The carry-lookahead adder is almost 3 times faster than the ripple-carry adder
Faster adders require more hardware and therefore are more expensive and power-hungry
  these trade-offs must be considered when choosing an appropriate adder for a design

## Slide 17: Subtractor
Performed by taking the two’s complement of the second number, then adding
To compute Y = A − B
  first create the two’s complement of B
    invert the bits of B to obtain B
    add 1 to get −B = B + 1
  add this quantity to A
    Y = A + B + 1 = A − B
We can use a single carry-lookahead adder by adding A + B with Cin = 1

## Slide 18: Comparators (1)
Determines whether two binary numbers are equal or if one is greater or less than the other
  receives two N-bit binary numbers A and B
  an equality comparator produces a single output, indicating A is equal to B
  a magnitude comparator produces one or more outputs, indicating the relative values of A and B
The equality comparator is the simpler piece of hardware
  it checks whether the corresponding bits in each column of A and B are equal
    using XNOR gates
  the numbers are equal if all of the columns are equal

## Slide 19: Comparators (2)
Magnitude comparison of signed numbers is usually done by computing A − B and looking at the sign (most significant bit) of the result
  if the result is negative (i.e., the sign bit is 1), then A is less than B
  otherwise, A is greater than or equal to B
This comparator functions incorrectly upon overflow
  overflow occurs when the two inputs have different signs and the sign of the subtraction result has a different sign than the A input

## Slide 20: Arithmetic/Logical Unit (1)
ALU combines a variety of mathematical and logical operations into a single unit
  addition, subtraction, AND, and OR operations
  control signal to specifies the function to perform
  the heart of most computer systems
The following implementation contains
  an N-bit adder, N 2-input AND and OR gates
More specifically
  if ALUControl=00, the multiplexer chooses A + B
  If ALUControl=01, the ALU computes A − B
  If ALUControl=10, the ALU computes A AND B
  If ALUControl=11 the ALU performs A OR B

## Slide 21: Arithmetic/Logical Unit (2)
ALU can produce flags to provide information about the result
Z (zero)
  all of the bits of the output are 0
N (negative)
  the most significant bit of the output
C (carry)
  adder produces a carry out and the ALU is performing addition or subtraction
V (overflow)
  overflow occurs when the addition of two same signed numbers produces a result with the opposite sign
    ALU is performing addition or subtraction (ALUControl1=0)
    A and Sum have opposite signs
    A and B have the same sign and the adder is performing addition (ALUControl0=0)
    or A and B have opposite signs and the adder is performing subtraction (ALUControl0=1)

## Slide 22: Arithmetic/Logical Unit (3)

## Slide 23: Arithmetic/Logical Unit (4)
The ALU flags can also be used for comparisons
  if Z is asserted, the result is 0, so A = B. Otherwise, A is not equal to B
  magnitude comparison is messier and depends on whether the numbers are signed or unsigned
Many variations on this basic ALU exist that support other functions

## Slide 24: Shifters (1)
Shifters move bits
  logical shifter (>> <<): shifts the number to the left or right and fills empty spots with 0
    11001 >> 2 = 00110; 11001 << 2 = 00100
  arithmetic shifter (>>> <<<): on right shifts fills the most significant bits with a copy of the old most significant bit (msb)
    useful for multiplying and dividing signed numbers
    11001 >>> 2 = 11110; 11001 << 2 = 00100
A left shift is a special case of multiplication
  a left shift by N bits multiplies the number by 2N
  0000112 << 4 = 1100002 is equivalent to 310 × 24 = 4810
An arithmetic right shift is a special case of division
  an arithmetic right shift by N bits divides the number by 2N
  111002 >>> 2 = 111112 is equivalent to −410/22 = −110

## Slide 25: Shifters (2)
An N-bit shifter can be built from N N:1 multiplexers
  depending on the value of a 2-bit shift amount control signal, the output receives the input shifted by 0 to 3 bits

## Slide 26: Rotators
Rotator rotates (left or right) a number in a circle such that empty spots are filled with bits shifted off the other end
  11001 ROR 2 = 01110
  11001 ROL 2 = 00111

## Slide 27: Multiplier
A N×N multiplier multiplies two N-bit numbers and produces a 2N-bit result
  multiplication of 1-bit binary numbers is equivalent to the AND operation
  AND gates are used to form the partial products
Considering an unsigned 4 × 4 multiplier
  partial product is a single multiplier bit (B3, B2,…) AND the multiplicand bits (A3, A2,…)
  partial product is added to the shifted next partial product
    B0 AND (A3, A2, A1, A0) is added to B1 AND (A3, A2, A1, A0)
  subsequent rows form and add the remaining partial product
For N-bit operands, there are N partial products and N − 1 stages of 1-bit adders

## Slide 28: Division
The most complex operation to perform among all the arithmetic operations
  it should be used as infrequently as possible
  A/B = Q + R/B
Numerous research works have been carried out to efficiently implement the division operation
  for the implementation, recall that R+B+1 = R−B
The delay increases proportionally to N2
R′ = 0
for i = N−1 to 0
R = {R′ << 1, Ai}
D = R − B
if D < 0 then
Qi = 0,
R′ = R
else
Qi = 1,
R′ = D
R = R′

## Slide 29: Floating-Point Addition (1)
1. Extract exponent and fraction bits
2. Prepend leading 1 to form the mantissa
3. Compare exponents
4. Shift smaller mantissa if necessary
5. Add mantissas
6. Normalize mantissa and adjust exponent if necessary
7. Round result
8. Assemble exponent and fraction back into floating-point number

## Slide 30: Floating-Point Addition (2)
Floating-point arithmetic is usually done in hardware to make it fast
  floating-point unit (FPU)
  typically distinct from the central processing unit (CPU)
The infamous floating-point division bug in the Pentium FPU cost Intel $475 million to recall and replace defective chips

## Slide 31: Exercises (1)
Ex1: Implement the following function using (a) an 8:1 multiplexer, (b) a 4:1 multiplexer and one inverter, and (c) a 2:1 multiplexer and two other logic gates
  Solution:

## Slide 32: Exercises (2)
Ex2: Implement the following function using (a) an 8:1 multiplexer, (b) a 4:1 multiplexer and no other gates, and (c) a 2:1 multiplexer, one OR gate, and an inverter
  Solution:

## Slide 33: Exercises (3)
Ex3: Design the following comparators for 32-bit unsigned numbers and sketch the schematics: (a) not equal, (b) greater than or equal to, (c) less than
  Solution: