## Slide 1: Sequential Circuits

## Slide 2: Index
Sequential Logic
Bistable element
SR Latch
D Latch
Clock
D Flip-Flop
Register
Enabled Flip-Flop
Resettable Flip-Flop
Transistor-Level Design
Astable circuits
Race Condition
Asynchronous circuits
Synchronous circuits
Synchronous vs Asynchronous Circuits

## Slide 3: Sequential Logic
The output of combinational logic depends only on current input values
  given a specification in the form of a truth table or boolean equation, we can create an optimized circuit to meet the specification
The outputs of sequential logic depend on both current and prior input values
  has memory
  explicitly remember previous inputs or it might distil the prior inputs into a smaller amount of information called the state of the system
    a set of bits (state variables) that contain all the information about the past necessary to explain the future behaviour of the circuit
  latches and flip-flops are simple sequential circuits that store one bit of state
Sequential circuits are complicated to analyse
  we can discipline ourselves to build only synchronous sequential circuits
  combinational logic and banks of flip-flops containing the state of the circuit

## Slide 4: Bistable element (1)
The fundamental building block of memory: an element with two stable states
  The inverters are cross-coupled
    the input of I1 is the output of I2 and vice versa
    the circuit has no inputs, but it does have two outputs
This circuit is cyclic
  Case 1: Q = 0
    I2 receives a FALSE input, so it produces a TRUE output on Q
    I1 receives a TRUE input, so it produces a FALSE output on Q
    this is consistent with the original assumption (Q = 0), so it is stable
  Case 2: Q = 1
    I2 receives a TRUE input and produces a FALSE output on Q
    I1 receives a FALSE input and produces a TRUE output on Q
    this is again stable
Because the cross-coupled inverters have two stable states, the circuit is said to be bistable

## Slide 5: Bistable element (2)
An element with N stable states conveys log2N bits of information, so a bistable element stores one bit
  state of the cross-coupled inverters is contained in one binary state variable (Q or Q)
  the value of Q tells us everything about the past that is necessary to explain the future behaviour of the circuit
    if Q=0, it will remain 0 forever
    if Q=1, it will remain 1 forever
When power is first applied to a sequential circuit, the initial state is unknown and usually unpredictable
  it may differ each time the circuit is turned on
Although the cross-coupled inverters can store a bit of information, they are not practical because the user has no inputs to control the state

## Slide 6: SR Latch (1)
Two cross-coupled NOR gates
Similar to the cross-coupled inverters, but its state can be controlled through the inputs
  set (S) and reset (R) the output
Case 1: R=1, S=0
  N1 sees at least one TRUE input R, so it produces a FALSE output on Q
  N2 sees both Q and S FALSE, so it produces a TRUE output on Q
Case 2: R=0, S=1
  N1 receives inputs of 0 and Q, however we don’t yet know Q
  N2 receives at least one TRUE input S, so it produces a FALSE output on Q
  Now we can revisit N1, so the output Q is TRUE.

## Slide 7: SR Latch (2)
Case 3: R=1, S=1
  N1 and N2 both see at least one TRUE input, so each produces a FALSE output
Case 4: R=0, S=0
  N1 receives inputs of 0 and Q, however we don’t yet know Q
  N2 receives inputs of 0 and Q. however we don’t yet know Q
  now we are stuck, but we know that Q must either be 0 or 1
Case 4a: Q=0
  N2 produces a TRUE output on Q
  N1 receives one TRUE input (Q), so its output is FALSE, just as we had assumed
Case 4b: Q=1
  N2 produces a FALSE output on Q
  N1 receives two FALSE inputs, so its output is TRUE, just as we had assumed
Putting this all together: if Q has some known prior value (Qprev), when R and S are 0, Q will remember this old value
  this circuit has memory

## Slide 8: SR Latch (3)
The truth table summarizes these four cases
The inputs S and R stand for Set and Reset
  “set” a bit means to make it TRUE
  “reset” a bit means to make it FALSE
When neither input is asserted, Q remembers its old value
Asserting both S and R simultaneously doesn’t make sense
  it means the latch should be set and reset at the same time
  the confused circuit responds by making both outputs 0

## Slide 9: D Latch
SR latch is awkward
  it behaves strangely when both S and R are simultaneously asserted
  moreover, S and R conflate the issues of what and when
    asserting one input determines what the state should be and when it should change
Design is easier when these questions (what and when) are separated
The D latch avoids the strange case of simultaneously asserted R and S inputs
  data input D controls what the next state should be
  clock input CLK controls when the state should change
  if CLK=0, S and R are FALSE (regardless of D) and Q remembers its old value
  if CLK=1, one AND is TRUE and the other is FALSE (depending on D) and Q = D
  In all cases, Q is the complement of Q

## Slide 10: Clock
The clock controls when data flows through the latch
  when CLK = 1, the latch is transparent
    data at D flows through to Q as if the latch were just a buffer
  when CLK = 0, the latch is opaque
    it blocks the new data from flowing through to Q, and Q retains the old value

## Slide 11: D Flip-Flop
Two back-to-back D latches controlled by complementary clocks
  L1 is called the leader/master
  L2 is called the follower/slave
D flip-flop copies D to Q on the rising edge of the clock and remembers its state at all other times:
  when CLK=0, the leader is transparent and the follower is opaque
    the D value propagates through to N1
  when CLK=1, the leader goes opaque and the follower becomes transparent
    the value at N1 propagates through to Q, but N1 is cut off from D
The D input specifies what the new state will be, the clock edge indicates when the state should be updated

## Slide 12: Register
An N-bit register is a bank of N flip-flops that share a common CLK
  all bits of the register are updated at the same time
  registers are the key building block of most sequential circuits

## Slide 13: Enabled Flip-Flop
Another input called Enable to determine if data is loaded on the clock edge
  when Enable is TRUE, the flip-flop behaves like an ordinary D flip-flop
  when Enable is FALSE, the flip-flop ignores the clock and retains its state
Useful when we wish to load a new value into a flip-flop only some of the time, rather than on every clock edge
Two ways to construct it from a D flip-flop and an extra gate
  an input multiplexer:
    the value D pass if Enable is TRUE
    the old state is recycled if Enable is FALSE
  the clock can be gated
    if Enable is TRUE, the CLK toggles normally
    if Enable is FALSE, the CLK input is also FALSE
    notice that Enable must not change while CLK=1 or the flip-flop see a clock glitch (switch at an incorrect time)
    generally, performing logic on the clock is a bad idea

## Slide 14: Resettable Flip-Flop
Another input, called Reset
  when Reset is FALSE, the flip-flop behaves like an ordinary D flip-flop
  when Reset is TRUE, the flip-flop ignores D and resets the output to 0
Useful when we want to force a known state into all the flip-flops in a system when we first turn it on
We can construct a it from an ordinary D flip-flop and an AND gate
  the Reset is an active low signal, meaning that it performs its function when it is 0
  by adding an inverter, the circuit could have accepted an active high reset signal

## Slide 15: Transistor-Level Design (1)
How many transistors are needed to build the D flip-flop?
  a NAND or NOR gate uses 4 transistors
  a NOT gate uses 2 transistors
  an AND gate is built from a NAND and a NOT, so it uses 6 transistors
  the SR latch uses two NOR gates, or 8 transistors
  the D latch uses an SR latch, two AND gates, and a NOT gate, or 22 transistors
  the D flip-flop uses two D latches and a NOT gate, or 46 transistors!

## Slide 16: Transistor-Level Design (2)
Flip-flops require a large number of transistors when built from logic gates, but the fundamental role of a latch is to be transparent or opaque, much like a switch
A compact D latch can be constructed from a single transmission gate
  when CLK=1 and CLK=0, the transmission gate is ON, so D flows to Q and the latch is transparent
  when CLK=0 and CLK=1, the transmission gate is OFF, so Q is isolated from D and the latch is opaque
Two major limitations:
  when the latch is opaque, Q is not held at its value by any gates and it is called a floating node: after some time, noise and charge leakage may disturb the value of Q
  a spike of noise that pulls D to a negative voltage can turn on the nMOS transistor, making the latch transparent, even when CLK=0; likewise, a spike on D above VDD can turn on the pMOS transistor even when CLK=0
The general rule is that neither the input of a transmission gate nor the state node of a sequential circuit should ever be exposed to the outside world where noise is likely

## Slide 17: Transistor-Level Design (3)
A more robust (12-transistor) D latch used on modern commercial chips
However, it is outside the scope of this course…

## Slide 18: Flip-Flop and Latch comparison
Apply the D and CLK inputs below to a D latch and a D flip-flop and determine the output Q of each device
  assume a small delay for Q to respond to input changes
The initial value of Q is unknown, as indicated by the pair of horizontal lines
Consider the latch:
  on the first rising edge of CLK, D=0 so Q definitely becomes 0
  each time D changes while CLK=1, Q follows
  when D changes while CLK=0, D is ignored
consider the flip-flop:
  on each rising edge of CLK, D is copied to Q
  at all other times, Q retains its state

## Slide 19: Astable circuits
Consider the three inverters tied in a loop
  each inverter has a propagation delay of 1ns
Suppose X is initially 0, then Y=1, Z=0, and, hence, X=1
  which is inconsistent with original assumption
  the circuit has no stable states and is said to be unstable or astable
The period of the oscillator depends on the propagation delay
  if X rises at t=0, Y falls at 1ns, Z rises at 2ns, and X falls at 3ns
  in turn, Y rises at 4ns, Z falls at 5ns, and X rises again at 6ns
  then, the pattern will repeat: each node oscillates with a period of 6 ns
  this circuit is called a ring oscillator
The gate delay depends on how the inverter was manufactured, the power supply voltage, and even the temperature
  the ring oscillator period is difficult to accurately predict

## Slide 20: Race Condition
Consider the following circuits, it seems a good implementation of a D latch (it use fewer gates):
The circuit has a race condition that causes it to fail when certain gates are slower than others
  suppose that CLK=D=1, the latch is transparent and passes D through to make Q=1
  now, CLK falls; the latch should remember its old value, keeping Q=1
  however, if the delay through the inverter is longer than delays of AND and OR
    N1 and Q may both fall before CLK rises
    N2 will never rise and Q becomes stuck at 0

## Slide 21: Asynchronous circuits
The previous examples contain loops called cyclic paths
  outputs are directly fed back to inputs
The behaviour depends on which of two paths through logic gates is fastest
  asynchronous circuits
  a circuit works, an identical one built of gates with different delays may not work
  a circuit works only at certain temperatures at which the delays are just right
  these malfunctions are extremely difficult to track down
We break the cyclic paths by inserting registers
  transforms the circuit into a collection of combinational logic and registers
  registers contain the state of the system, which changes only at the clock edge
  the state is synchronized to the clock
  if the clock is sufficiently slow all races are eliminated
    inputs to all registers settle before the next clock edge

## Slide 22: Synchronous circuits (1)
A synchronous sequential circuit has a clock input, whose rising edges indicate a sequence of times at which state transitions occur
  current state and next state distinguish the state of the system at the present from the state to which it will enter on the next clock edge
Rules of synchronous sequential circuit composition
  a circuit is a synchronous if it consists of interconnected elements, such that
    every element is either a register or a combinational circuit
    at least one circuit element is a register
    all registers receive the same clock signal
    every cyclic path contains at least one register
A flip-flop is the simplest synchronous sequential circuit
  it has one input, one clock, one output, and two states
  the next state is D and the output Q is the current state

## Slide 23: Synchronous circuits (2)
Which of the following circuits are synchronous sequential circuits?
  (a) is combinational
    it has no registers
  (b) is sequential with no feedback
  (c) no combinational, no synchronous
    it has a latch that is neither a register nor a combinational circuit
  (d) (e) are synchronous sequential logic
  (f) no combinational, no synchronous sequential
    it has a cyclic path but no register in the path
  (g) is synchronous sequential logic
  (h) is not, strictly speaking, a synchronous sequential circuit
    the second register receives a different clock signal than the first, delayed by two inverter delays

## Slide 24: Synchronous vs Asynchronous Circuits
Asynchronous design is more general than synchronous design
  the timing of the system is not limited by clocked registers
  just as analog circuits are more general than digital circuits
Synchronous circuits are easier to design than asynchronous circuits
  just as digital are easier than analog circuits
Despite decades of research on asynchronous circuits, virtually all digital systems are essentially synchronous
Asynchronous circuits are occasionally necessary when communicating between systems with different clocks or when receiving inputs at arbitrary times
  just as analog circuits are necessary when communicating with the real world of continuous voltages

## Slide 25: Exercises (1)
Ex09.1: Given the input waveforms below, sketch the output of an SR latch
  Solution:

## Slide 26: Exercises (2)
Ex09.2: Given the input waveforms below, sketch the output of an D latch
  Solution:

## Slide 27: Exercises (3)
Ex09.3: The toggle (T) flip-flop has one input, CLK, and one output, Q. On each rising edge of CLK, Q toggles to the complement of its previous value. Draw a schematic for a T flip-flop using a D flip-flop and an inverter?
  Solution:

## Slide 28: Exercises (4)
Ex09.4: A JK flip-flop receives a clock and two inputs, J and K. On the rising edge of the clock, it updates the output, Q. If J and K are both 0, Q retains its old value. If only J is 1, Q becomes 1. If only K is 1, Q becomes 0. If both J and K are 1, Q becomes the opposite of its present state. (a) Construct a JK flip-flop, using a D flip-flop and some combinational logic. (b) Construct a D flip-flop, using a JK flip-flop and some combinational logic.
  Solution: