## Slide 1: Timing

## Slide 2: Index
Propagation and Contamination Delay
Critical paths
Glitches
Wire delay
Timing of sequential logic
Dynamic Discipline
Timing Specification
System Timing
Setup Time and Hold Time Constraints
Timing Analysis
Fixing Hold Time Violations
Clock Skew
Metastability
Resolution Time
Synchronizers
System reliability

## Slide 3: Delay
One of the most challenging issues in circuit design is timing
  making a circuit run fast
An output takes time to change in response to an input change
  circuit delays are on the order of picoseconds (10−12) to nanoseconds (10−9)
Timing diagram
  the transient response of the buffer circuit when an input changes
  transition from LOW to HIGH is called the rising edge
  transition from HIGH to LOW is called the falling edge
  The blue arrow indicates that the rising edge of Y depends on the rising edge of A
Delay is measured from 50% point of the input to 50% point of the output

## Slide 4: Propagation and Contamination Delay
propagation delay tpd
  maximum time from when the input changes until the output reaches its final value
contamination delay tcd
  minimum time from when the input changes until the output starts to change its value
The figure shows that A is initially either HIGH or LOW and changes to the other state at a particular time
  we are interested only in the fact that it changes, not what value it has
In response, Y changes some time later
  Y starts to change tcd after A transitions
  Y definitely settles to its new value within tpd.
The causes of delay include the time required to charge the capacitance in a circuit and the speed of light
  calculating tpd and tcd requires delving into the lower levels of abstraction
  manufacturers supply data sheets specifying these delays for each gate

## Slide 5: Critical path
Delays are also determined by the path a signal takes from input to output
The critical path is the longest (slowest) path
  the input travels through more gates to the output
  it is “critical” because it limits the speed at which the circuit operates
  the propagation delay of a circuit is the sum of the propagation delay of all element on the critical path
    tpd = 2 tpd_AND + tpd_OR
The short path is the shortest (fastest) path
  the input travels through the minimum number of gates to the output
  the contamination delay is the sum of the contamination delays through each element on the short path
    tcd = tcd_AND

## Slide 6: Finding delays
Find the propagation delay and contamination delay of the following circuit
According to the datasheets, each gate has a propagation delay of 100ps and a contamination delay of 60ps
The critical path is from input A or B through three gates to the output Y
  hence, tpd is three times the propagation delay of a single gate, 300ps
The shortest path is from input C, D, or E through two gates to the output Y
  so tcd is 120ps

## Slide 7: Control-critical vs data-critical
Compare the worst-case timing of the two four-input multiplexer designs (two-level logic vs multiplexer logic)
Critical paths:
  two-level logic is control critical: the critical path is from the control to the output
  multiplexer logic is data critical: the critical path is from the inputs to the output
  if data arrive before the control, we prefer the design with the shortest control delay
  if the control arrive before the data, we prefer the design with the shortest data delay
The best choice depends on the power, cost, and availability of parts

## Slide 8: Glitches (1)
It is possible that a single input transition can cause multiple output transitions: glitches or hazards
Transition across the boundary of two prime implicants in the K-map indicates a possible glitch
As long as we wait for the propagation delay to elapse before we depend on the output, glitches are not a problem

## Slide 9: Glitches (2)
The DEEDS simulator take into account the propagation delay (5ns):
and this glitch effect can be seen in the simulation (zooming enough):

## Slide 10: Glitches (3)
We can eliminate glitches by adding redundant implicants to the K-map to cover these boundaries
  at the cost of extra hardware
However, simultaneous transitions on multiple inputs can also cause glitches that cannot be fixed by adding hardware
The vast majority of interesting systems have these simultaneous transitions, then glitches are a fact of life in most circuits
The point is not to eliminate them but to be aware that they exist
  this is especially important when looking at timing diagrams on a simulator or oscilloscope

## Slide 11: Wire delay
We have assumed that wires are equipotential connections that have a single voltage along their entire length
However, signals propagate along wires at the speed of light in the form of electromagnetic waves
  if wires are short enough or signals change slowly, the assumption is good enough
  when wires are long or signals are very fast, the transmission time along the wire becomes important to accurately determine the circuit delay
We model such wires as transmission lines
  in which a wave of voltage and current propagates at the speed of light
  when the wave reaches the end of the line, it may reflect back along the line, causing noise and odd behaviours
Whenever the wire delay is shorter than a fraction (typically 20%) of the edge rates (rise or fall times) of a signal it has an insignificant effect

## Slide 12: Timing of sequential logic
A flip-flop copies input D to output Q on the rising edge of the clock (sampling)
  if D is stable (0 or 1) when the clock rises, the behaviour is clearly defined
  what happens if D is changing at the same time the clock rises?
The problem is similar to that faced by a camera when snapping a picture
  it is characterized by its aperture time, during which the object must remain still for a sharp image to be captured
A sequential element has an aperture time around the clock edge, during which the input must be stable for the flip-flop to produce a well-defined output
  setup time before the clock edge
  hold time after the clock edge
As the static discipline (limits us to using logic levels outside the forbidden zone), the dynamic discipline limits us to signals that change outside the aperture time
  we can think of time in discrete units called clock cycles, just as we think of signal levels as discrete 1’s and 0’s
  a signal may glitch and oscillate for some bounded amount of time, we are concerned only about its final value at the end of the clock cycle

## Slide 13: Dynamic Discipline
We can write A[n] (the value of signal A at the end of the n-th clock cycle, rather than A(t), where t is any real number
  the clock period has to be long enough for all signals to settle
  a limit on the speed of the system
In real systems, the clock does not reach all flip-flops at precisely the same time
  clock skew
  further increases the necessary clock period
Sometimes it is impossible to satisfy the dynamic discipline, especially when interfacing with the real world
  consider a circuit with an input coming from a button, we might press the button just as the clock rises
  this result in a phenomenon called metastability
    flip-flop captures a value between 0 and 1
    that can take an unlimited amount of time to resolve into a good logic value

## Slide 14: Timing Specification
When the clock rises, the output…
…may start to change after the clock-to-Q contamination delay (tccq)
  the fastest delays through the circuit
…will definitely settle to the final value within the clock-to-Q propagation delay (tpcq)
  the slowest delays through the circuit
The input…
  ….must have stabilized at least setup time (tsetup) before the rising edge of the clock
  …must remain stable for at some hold time (thold) after the rising edge of the clock
The sum of setup and hold times is called the aperture time of the circuit, because it is the total time for which the input must remain stable

## Slide 15: System Timing
The clock period or cycle time (Tc) is the time between rising edges of a repetitive clock signal
Its reciprocal fc = 1/Tc is the clock frequency
  measured in units of Hertz (Hz) or cycles per second
  increasing frequency increases the work a digital system can accomplish per unit time
Consider a generic path in a synchronous sequential circuit
  output signals may start to change a contamination delay after input changes
    grey arrows
  output signals settles to the final value within a propagation delay after its input settles
    blue arrows
We can analyse the timing constraints with respect to the setup and hold time of the second register

## Slide 16: Setup Time Constraint
To satisfy the setup time of R2, D2 must settle no later than the setup time before the next clock edge
  minimum clock period
  Tc > tpcq + tpd + tsetup
In commercial designs, usually the only variable under the control of the designer is the maximum propagation delay through the combinational logic
  clock period is dictated by the marketing department (to ensure a competitive product)
  the flip-flop delay and setup time are specified by the manufacturer
  tpd > Tc - (tpcq + tsetup)
  if the propagation delay through the combinational logic is too long, its output may not have settled to final value by the time next input needs it to be stable
Ideally, the entire cycle time Tc would be available for useful computation in the combinational logic. The sequencing overhead (tpcq + tsetup) cuts this time

## Slide 17: Hold Time Constraint
To satisfy the hold time of R2, D2 must not change until the hold time after the rising edge of the clock
  tccq + tcd > thold
Again, tccq and thold are characteristics of the flip-flop that are usually outside the designer’s control
Minimum contamination delay through the combinational logic
  tcd > thold – tccq
We expect that two flip-flops may be directly cascaded
  in such a case, tcd=0 (no combinational logic) in between and thold < tccq
  a reliable flip-flop must have a hold time shorter than contamination delay
  often, flip-flops are designed with thold=0
We usually ignore the hold time constraint
  nevertheless, it is critically important
  if violated, the only solution is to increase the contamination delay through the logic
    which requires redesigning the circuit
  unlike setup time constraint, it cannot be fixed by adjusting the clock period

## Slide 18: Timing Analysis (1)
Sequential circuits have setup and hold time constraints that dictate the maximum and minimum delays of the combinational logic between flipflops
  modern flip-flops are usually designed so that the minimum delay through the combinational logic can be 0
  the maximum delay constraint limits the number of consecutive gates on the critical path of a circuit
Consider the circuit in figure and determine the maximum clock frequency and whether any time violations could occur
  Flip-flops: tccq=30ps; tpcq=80ps; tsetup=50ps; thold=60ps
  Logic gates: tcd=25ps; tpd=40ps

## Slide 19: Timing Analysis (2)
Critical path:
  B=1, C=0, D=0, A rises from 0 to 1, triggering n1 to rise, X′ to rise, and Y′ to fall
  assume gates require full propagation delay
  three gate delays
  Y′ must set up before the next rising edge of the CLK
Maximum clock frequency:
  Tc>tpcq+tpd+tsetup= 80ps+3*40ps+50ps= 250ps
  fc = 1/Tc = 4 GHz
  tccq=30ps; tpcq=80 ps; tsetup=50 ps; thold=60 ps
  tpd=40 ps; tcd=25 ps

## Slide 20: Timing Analysis (3)
Shortest path:
  A=0; C rises, causing X′ to rise
  assume gates switch after only contamination delay
  only one gate delay
Hold Time Constraint
  thold < tccq + tcd = 30ps + 25ps = 55ps
  thold = 60ps
  the circuit has a hold time violation and may behave erratically at any clock frequency
  tccq=30ps; tpcq=80 ps; tsetup=50 ps; thold=60 ps
  tpd=40 ps; tcd=25 ps

## Slide 21: Fixing Hold Time Violations
A possible solution is to add buffers to slow down the short paths
Short paths are slowed by the contamination delay of the buffer
  X′ will not change until tccq + 2*tcd = 30ps+2*25ps = 80ps > thold
Critical path is unaffected because it does not pass through any buffers
  the maximum clock frequency is still 4 GHz
In general, adding buffers can usually (not always) solve hold time problems without slowing the critical path
  the example had an unusually long hold time to illustrate the problems
  most flip-flops are designed with thold < tccq to avoid such problems

## Slide 22: Clock Skew (1)
We assumed that the clock reaches all registers at exactly the same time
In reality, there is some variation in this time
  the wires from the clock source to different registers may be of different lengths, resulting in slightly different delays
  noise also results in different delays
When doing timing analysis, we have to consider the worst-case scenario so that we can guarantee that the circuit will work under all circumstances
We can adds skew to the timing diagram
  heavy clock line indicates the latest time at which the clock signal might reach any register
  hashed lines show that the clock might arrive up to tskew earlier

## Slide 23: Clock Skew (2)
First, consider the setup time constraint
  worst case: R1 receives the latest clock and R2 receives the earliest clock, leaving less time for data propagation
  Tc > tpcq + tpd + tsetup + tskew
  tpd < Tc − (tpcq + tsetup + tskew)
Next, consider the hold time constraint
  worst case: R1 receives an early clock and R2 receives a late clock
  data must not arrive until a hold time after the late clock
  tccq + tcd > thold + tskew
  tcd > thold + tskew − tccq
In summary, clock skew increases setup time and the hold time
  it reduce the time available for useful work in the combinational logic
  increases the minimum delay through the combinational logic: even if thold = 0, a pair of back-to-back flip-flops will violate the constrain if tskew > tccq

## Slide 24: Clock Skew (3)
Revisit the timing analysis example assuming a 50ps of clock skew
Critical path remains the same
  setup time is increased by the skew
  Tc > tpcq + tpd + tsetup + tskew= 80ps + 3*40ps + 50ps + 50ps = 300ps
  fc = 1/Tc = 3.33 GHz
Short path also remains the same at 55ps
  hold time is increased by the skew
  thold + tskew= 60 + 50 = 110 ps, which is much greater than 55 ps
Skew in the system just makes the violation worse
To fix the problem:
  more buffers could be inserted
  buffers would need to be added on the critical path as well, reducing the clock frequency
  alternatively, a flip-flop with a shorter hold time might be used

## Slide 25: Metastability (1)
It is not always possible to guarantee that the input to a sequential circuit is stable during the aperture time
  especially when the input arrives from the external world
Consider a button connected to the input of a flip-flop
  when the button is pressed much before CLK, Q = 1
  when the button is not pressed until long after CLK, Q = 0
  when the button is pressed between tsetup before CLK and thold after CLK, the input violates the dynamic discipline and the output is undefined
When a flip-flop samples an input changing during the aperture, output may momentarily go in forbidden zone
  metastable state
  eventually, it will resolve to a stable state, however, the resolution time required is unbounded

## Slide 26: Metastability (2)
The metastable state of a flip-flop is analogous to a ball on the summit of a hill between two valleys
  valleys are stable states, the top of the hill is metastable
  the ball would remain there if it were perfectly balanced, but because nothing is perfect, the ball will eventually roll to one side or the other
  the time required for this change to occur depends on how nearly well balanced the ball originally was
Every bistable device has a metastable state between the two stable states

## Slide 27: Resolution Time
The resolution time is a random variable
Theoretical and experimental analyses have shown that the probability that the resolution time exceeds some arbitrary time t decreases exponentially with t
  p(tres > t) = T0 / TC * exp (-t/τ)
  where TC is the clock period, and T0 and τ are characteristic of the flipflop
  the equation is valid only for t substantially longer than tpcq
This means that time required to resolve is unbounded, however if we wait long enough the flip-flop will reach a valid logic level

## Slide 28: Synchronizers (1)
Asynchronous inputs to digital systems from the real world are inevitable
  human input is asynchronous
  can lead to metastable voltages and erratic system failures
Ensure that the probability of encountering a metastable voltage is “small”
  cell phone: one failure in 10 years is acceptable, the user can turn the phone off and on
  medical device, one failure in the expected life of the universe is a better target
A synchronizer is a device that receives an asynchronous input D and a clock CLK and produces a valid output Q with high probability
  If D is stable during the aperture, Q should take on the same value as D
  If D changes during the aperture, Q may take HIGH or LOW, but must not be metastable

## Slide 29: Synchronizers (2)
We can build a simple synchronizer out of two flip-flops
  F1 samples D on the rising edge of CLK
  if D is changing at that time, the output D2 may be momentarily metastable
  if clock period is long enough, D2 (with high probability), resolve to a valid logic level
  F2 samples D2 (now stable), producing a good output Q
The synchronizer fails if Q becomes metastable
  if D2 has not resolved to a valid level by the time tres > TC − tsetup
The probability of failure for a single input is
  p(failure) = T0 / TC * exp (-(TC-tsetup)/τ)
If D changes N times per second, the probability of failure per second is
  P(failure)/sec = N * p(failure)

## Slide 30: System reliability
It is measured in mean time between failures (MTBF)
  the average amount of time between failures of the system
  the reciprocal of the probability that the system will fail in any given second
  MTBF = 1 / p(failure)/sec = TC/NT0 * exp ((TC-tsetup)/τ)
MTBF improves exponentially as the synchronizer waits for a longer time
  for most systems, to wait for one clock cycle provides a safe MTBF
  in exceptionally high-speed systems, waiting for more cycles may be necessary
A system receives asynchronous inputs from the sensors on average 0.2 times per second. How long must be the clock period for the MTBF to exceed 1 year?
  the flip-flops in the synchronizer have the following characteristics: τ=200ps, T0=150ps, and tsetup=500ps
  3.14 107 sec = TC/(0.2 * 150 10-12) * exp ((TC – 500 10-12) / 200 10-12)
  no closed form solution, however, it is easy enough to solve by guess and check
  Tc = 3.036 ns

## Slide 31: Exercises (1)
Ex1: Determine the propagation delay and contamination delay of the following circuits using the provided gate delays
  Solution:
    tpd = 3 tpd_NAND2 = 60 ps
    tcd = tcd_NAND2 = 15 ps
    tpd = tpd_NAND2 + 2 tpd_NOR2 + tpd_NAND2 = 30 + 2*30 + 20 = 110 ps
    tcd = 2 tcd_NAND2 + tcd_NOR2 = 2*15 + 25 = 55 ps

## Slide 32: Exercises (2)
Ex2: Sketch a schematic for a fast 3:8 decoder. Suppose gate delays are the same of the previous exercise. Design your decoder to have the shortest possible critical path and indicate what that path is. What are its propagation delay and contamination delay?
  Solution:
          tpd = tpd_NOT + tpd_AND3 = 15 + 40 = 55 ps
          tcd = tcd_NAND3 = 30 ps

## Slide 33: Exercises (3)
Ex3: Consider the circuit in figure to compute a registered four-input XOR function. Gates have a tpd=100ps and a tcd=55ps. Flip-flops have a tsetup=60ps, a thold=20ps, tpcq=70ps, and a tccq=50ps
  (a) if there is no clock skew, what is the maximum frequency?
  (b) how much clock skew can the circuit tolerate at 2 GHz?
  (c) how much clock skew can the circuit tolerate before a hold time violation?
  Solution: