## Slide 1: Data Representation

## Slide 2: Index
Number Systems
  Decimal Numbers
  Binary Numbers
  Decimal to binary conversion
  Hexadecimal Numbers
Data Units and Scaling
  Bytes, nibble and words
  Kilo, Mega and Giga
Arithmetic with Binary Numbers
  Binary addition
  Sign/magnitude numbers
  Two’s complement format
  Multiplication
Fractional Numbers
  Fixed-Point Number Systems
  Floating-Point Number Systems

## Slide 3: Decimal Numbers
In elementary school, we learned to do arithmetic in decimal
  just as we have ten fingers, there are ten digits: 0, 1, 2, …, 9
Decimal digits are joined together to form longer numbers
  each column has ten times the weight of the previous column
  from right to left, the column weights are 1, 10, 100, 1000, and so on
Decimal numbers are referred to as base 10
An N-digit decimal number represents one of 10N possibilities
  range of the number
  a three-digit number represents one of 1000 possibilities in the range 0 to 999

## Slide 4: Binary Numbers
Bits are joined together to form binary numbers
  a column of a binary number has twice the weight of the previous column (base 2)
  1, 2, 4, 8, 16, 32, 64, 128, 256, 512, 1.024, 2.048, 4.096, 8.192, 16.384, 32.768, 65.536
An N-bit number represents one of 2N possibilities

## Slide 5: Decimal to binary conversion (1)

## Slide 6: Decimal to binary conversion (2)

## Slide 7: Hexadecimal Numbers
Writing long binary numbers becomes tedious and prone to error
Notice: a group of four bits represents one of 24 = 16 possibilities
  it is convenient to work in base 16
  digits 0 to 9 along with the letters A to F
Each hexadecimal digit directly corresponds to four binary digits

## Slide 8: Bytes, nibble and words
A group of eight bits is called byte
  it represents one of 28 = 256 possibilities
  size of objects stored in memories is measured in bytes
A group of four bits is called nibble
  it represents one of 24 = 16 possibilities
  a hexadecimal digit stores one nibble
Microprocessors handle data in chunks called words
  the size of a word depends on the architecture of the microprocessor
  most computers had 64-bit processors (64-bit words)
  older computers handling 32-bit words were also widely available
Within a group of bits…
  …the bit in the first column (on the right) is called the least significant bit (lsb)
  …the bit at the other end (on the left) is called the most significant bit (msb),
Similarly, within a word:
  least significant byte (LSB)
  most significant byte (MSB)

## Slide 9: Kilo, Mega and Giga
The powers of two line up nicely with powers of ten: 210 = 1024 ≈ 103
  kilo indicates 210 ≈ 103
  mega (million) indicates 220 ≈ 106
  giga (billion) indicates 230 ≈ 109
IEC (International Electrotechnical Commission) makes a distinction
  kibibyte (KiB = 1024 B), mebibyte (MiB = 1024^2 B), Gibibyte (GiB = 1024^3 B)
  kilobyte (KB = 1000 B), megabyte (MB = 1000^2), gigabyte (GB = 1000^3)
  However, in common usage KB, MB, and GB are still often used with base 2
Using these approximation, it is easy to estimate any power of two
  remember this: 1, 2, 4, 8, 16, 32, 64, 128, 256, 512
  split the exponent into a multiple of ten and the remainder

## Slide 10: Binary Addition
Like decimal addition, but easier
  if the sum of two numbers is greater than what fits in a single digit (1)
  we carry a 1 into the next column (carry bit)
We are no in the purely mathematical realm
  we are dealing with real systems
  we operate on a fixed number of digits, so additions can overflow
  if the result is too big to fit in the available digits
Overflow can be detected: check for a carry out of the MSB

## Slide 11: Sign/magnitude Numbers
Binary subtraction
  mathematically simple, like addition
  in hardware, supporting both would require two circuits (adder + subtractor)
  subtraction can be rewritten as addition with a negative number: A – B = A + (-B)
  this can reduce both to one operation: addition
  requires a representation for negative numbers
Sign/magnitude
  use the MSB as the sign and the remaining N−1 bits as the magnitude
    a sign bit of 0 indicates positive, a sign bit of 1 indicates negative
  intuitively appealing: match our way of writing negative numbers with a minus sign followed by the magnitude
  problems:
    ordinary binary addition does not work
    it is odd that both +0 and −0 exist, both indicate zero

## Slide 12: Two’s complement representation (1)
Two’s complement representation
  exactly unsigned numbers, except that the MSB has a negative weight
Notice that the most significant bit can be viewed as the sign bit

## Slide 13: Two’s complement representation (2)
Addition works properly for both positive and negative numbers
  when adding N-bit numbers, the carry of the Nth bit is discarded
Subtraction is performed as A-B = A + (-B)
Zero has only one representation (avoiding the redundancy)
The range of an N-bit two’s complement number spans [−2N−1, 2N−1 − 1]
  there is one more negative number than positive number (because there is no −0)
  it is called the weird number (it has no positive counterpart)

## Slide 14: Two’s complement representation (3)
Procedure to obtain the two’s complement representation of a negative number :
  take the binary representation of the positive number (the magnitude)
  invert all the bits (this is called the one’s complement)
  add 1 to the result
We can reverse the procedure to get the magnitude of a negative number

## Slide 15: Two’s complement representation (4)
When a two’s complement number is extended to more bits, the sign bit must be copied into the most significant bit positions (sign extension)
Comparison:

## Slide 16: Detecting Overflow in Signed Addition
Cannot detect overflow by just checking the final carry (unlike unsigned).
Overflow happens only when adding two numbers with the same sign.
Rule of thumb:
  positive + negative or negative + positive -> no overflow
  positive + positive -> must stay positive
  negative + negative -> must stay negative
  if the result flips sign, the true value exceeded the representable range -> overflow

## Slide 17: Multiplication
Multiplication of unsigned binary numbers is like decimal multiplication but involves only 1 and 0
  partial products are formed by multiplying a single digit of the multiplier with the entire multiplicand
  the shifted partial products are summed to form the result
The result of multiplying an M-bit number by an N-bit number may require up to M+N bits
Partial products in the binary case are either the multiplicand or all 0

## Slide 18: Fractional Numbers
Computers operate on both integers and fractions
  we have only considered representing signed or unsigned integers
  fixed- and floating-point number systems that can represent rational numbers
Fixed-point numbers are analogous to decimals
  some of the bits represent the integer part, and the rest represent the fraction
Floating-point numbers are analogous to scientific notation
  with a mantissa and an exponent

## Slide 19: Fixed-Point Number Systems
It has an implied binary point between the integer and fraction bits
  analogous to the point between the integer and fraction digits of a decimal number
  0110.1100 = 22+21+2-1+2-2 = 6.75
Signed fixed-point numbers can use either
  sign/magnitude notation: the most significant bit is used to indicate the sign
    -2.375 = 1010.0110
  two’s complement:
    -2.375 = 1101.1010
Notice that fixed-point numbers are just a collection of bits
  there is no way of knowing the existence of the binary point
  only through agreement of those people interpreting the number
Standard formats
  Ua.b unsigned fixed-point number with a integer bits and b fraction bits
  Qa.b signed (two’s complement) fixed-point number with a integer bits b fractional bits
Commonly used in digital signal processing (DSP), graphics, and machine learning applications
  Q1.15 is the most common
  Q1.31 sometimes used for higher precision intermediate results
  U8.8 sometimes used for sensor readings

## Slide 20: Floating-Point Number Systems (1)
Analogous to scientific notation:
  the decimal point “floats" to the position right after the most significant digit
  allow the representation of very large and very small numbers
Historically, many incompatible formats -> poor portability
IEEE 754 (1985) introduced a universal standard: 32-bit single precision
Special cases:

## Slide 21: Floating-Point Number Systems (2)
So far, we have examined 32-bit floating-point numbers
  single-precision (float)
The IEEE 754 standard also defines other types
Today, growing importance of machine learning, new formats are emerging:
  Google BFloat16 (exponent: 8 bits, mantissa: 8 bits)
  IMB DLFloat16 (exponent: 6 bits, mantissa: 10 bits)
  NVIDIA FP8 (exponent: 4 bits, mantissa: 4 bits)
  Tesla CFloat8 (exponent: 5 bits, mantissa: 4 bits)
  NVIDIA FP4 (introduced in GPU Blackwell in 2024)